## Slide 1: Vergence: The Vergence Formula
Basic Optics, Chapter 3

## Slide 2
A +1D lens will focus parallel rays 1m to the right of the lens
+1D
1 meter
Distance = 1 m
Reciprocal = 1/1
Diopters = +1
    A -1D lens will ‘focus’ parallel rays1m to the left of the lens
-1D
-1 meter
Distance = -1 m
Reciprocal = 1/-1
Diopters = -1
(Remember, distances to the left of the lens are considered ‘minus’)
We have seen how the dioptric power of a lens affects incoming parallel rays.
Vergence: The Vergence Formula

## Slide 3
A +1D lens will focus parallel rays ?m to the ? of the lens
+1D
Diopters = +1
Reciprocal = ?
Distance = ?
    A -1D lens will ‘focus’ parallel rays ?m to the ? of the lens
-1D
Diopters = -1
Reciprocal = ?
Distance = ?
We have seen how the dioptric power of a lens affects incoming parallel rays. But what if the rays are not parallel?
?
?
non
non
^
^
Vergence: The Vergence Formula

## Slide 4
A +1D lens will focus parallel rays ?m to the ? of the lens
+1D
Diopters = +1
Reciprocal = ?
Distance = ?
    A -1D lens will ‘focus’ parallel rays ?m to the ? of the lens
-1D
Diopters = -1
Reciprocal = ?
Distance = ?
?
?
^
We have seen how the dioptric power of a lens affects incoming parallel rays. But what if the rays are not parallel?
We need a more generalized concept concerning the relationships among incoming/outgoing rays, and lenses.
Vergence: The Vergence Formula
^
non
non

## Slide 5
A +1D lens will focus parallel rays ?m to the ? of the lens
+1D
Diopters = +1
Reciprocal = ?
Distance = ?
    A -1D lens will ‘focus’ parallel rays ?m to the ? of the lens
-1D
Diopters = -1
Reciprocal = ?
Distance = ?
?
?
^
We have seen how the dioptric power of a lens affects incoming parallel rays. But what if the rays are not parallel?
We need a more generalized concept concerning the relationships among incoming/outgoing rays, and lenses.
This is provided by The Vergence Formula
Vergence: The Vergence Formula
^
non
non

## Slide 6
The Vergence Formula
Vergence: The Vergence Formula

## Slide 7
The Vergence Formula
  Crucial concept in optics
Vergence: The Vergence Formula

## Slide 8
The Vergence Formula
  Crucial concept in optics
  Describes the vergence relations among rays before, during and after encountering a refractive surface (e.g., lens)
Vergence: The Vergence Formula

## Slide 9
The Vergence Formula
  Crucial concept in optics
  Describes the vergence relations among rays before, during and after encountering a refractive surface (e.g., lens)
    Head’s up: We will also use the Vergence Formula in describing the relations among rays interacting with reflecting surfaces, i.e., mirrors
Vergence: The Vergence Formula

## Slide 10
The Vergence Formula
U + P = V
Vergence: The Vergence Formula

## Slide 11
The Vergence Formula
U + P = V
Vergence of
incoming light
(in diopters)
Vergence: The Vergence Formula

## Slide 12
The Vergence Formula
U + P = V
Vergence contributed
by lens (in diopters)
Vergence of
incoming light
(in diopters)
Vergence: The Vergence Formula

## Slide 13
The Vergence Formula
Vergence of
light leaving lens
(in diopters)
U + P = V
Vergence contributed
by lens (in diopters)
Vergence of
incoming light
(in diopters)
Vergence: The Vergence Formula

## Slide 14
The Vergence Formula
Vergence of
light leaving lens
(in diopters)
U + P = V
Vergence contributed
by lens (in diopters)
Vergence of
incoming light
(in diopters)
Vergence: The Vergence Formula
tl;dr The vergence of light leaving a lens is the sum of the vergence of the light entering the lens and the vergence contributed by the lens itself

## Slide 15
U + P = V
Parallel rays, therefore
U = 0
+1D
Vergence: The Vergence Formula

## Slide 16
+1D
U + P = V
Parallel rays, therefore
U = 0
+1D lens, therefore P = +1D
Vergence: The Vergence Formula
P=+1D

## Slide 17
+1D
U + P = V
Parallel rays, therefore
U = 0
Plugging these values into the Vergence Formula:
U + P = V
0 + (+1) = V
Vergence: The Vergence Formula
P=+1D
+1D lens, therefore P = +1D

## Slide 18
V = +1D
U + P = V
Parallel rays, therefore
U = 0
+1D
Plugging these values into the Vergence Formula:
U + P = V
0 + (+1) = V
+1 = V
Vergence: The Vergence Formula
P=+1D

## Slide 19
V = +1D
U + P = V
Parallel rays, therefore
U = 0
+1D
Plugging these values into the Vergence Formula:
U + P = V
0 + (+1) = V
+1 = V
Distance?
Vergence: The Vergence Formula
Distance equals the reciprocal of the outgoing vergence, ie, 1/V
P=+1D

## Slide 20
1/+1 = 1 meter
V = +1D
U + P = V
Parallel rays, therefore
U = 0
+1D
Plugging these values into the Vergence Formula:
U + P = V
0 + (+1) = V
+1 = V
Vergence: The Vergence Formula
Distance equals the reciprocal of the outgoing vergence, ie, 1/V
P=+1D

## Slide 21
U = 0
V = ?
U + P = V
+2D
Vergence: The Vergence Formula
P=+2D

## Slide 22
V = +2D
U = 0
U + P = V
Distance = ?
+2D
Vergence: The Vergence Formula
P=+2D

## Slide 23
V = +2D
U = 0
U + P = V
Distance = 1/2 = .5m
+2D
Vergence: The Vergence Formula
P=+2D

## Slide 24
U = ?
P=+3D
U + P = V
+3D
Vergence: The Vergence Formula
To determine the vergence U of the incoming light,
take the reciprocal of the distance from its source
or focal point:
-.4 meters

## Slide 25
U = 1/-.4m =
-2.5D
U + P = V
+3D
Vergence: The Vergence Formula
To determine the vergence U of the incoming light,
take the reciprocal of the distance from its source
or focal point:
U = 1/-.4m = -2.5D
-.4 meters
Remember, the vergence of
diverging rays is always negative!
P=+3D

## Slide 26
V = +0.5D
U = -2.5D
U + P = V
+3D
Vergence: The Vergence Formula
Plugging these values into the Vergence Formula:
U + P = V
-2.5 + (+3) = V
+0.5 = V
-.4 meters
P=+3D

## Slide 27
-.4 meters
U = -2.5D
U + P = V
+3D
Vergence: The Vergence Formula
Plugging these values into the Vergence Formula:
U + P = V
-2.5 + (+3) = V
+0.5 = V
Distance equals the reciprocal of the outgoing vergence, ie, 1/V
V = +0.5D
P=+3D
Distance = ?

## Slide 28
Distance = 1/.5 = 2m
-.4 meters
U = -2.5D
U + P = V
+3D
Vergence: The Vergence Formula
Plugging these values into the Vergence Formula:
U + P = V
-2.5 + (+3) = V
+0.5 = V
Distance equals the reciprocal of the outgoing vergence, ie, 1/V
V = +0.5D
P=+3D

## Slide 29
P =
-1D
U + P = V
-1D
Vergence: The Vergence Formula
-1 meter
U = 1/-1m
= -1D

## Slide 30
U + P = V
-1D
Vergence: The Vergence Formula
Plugging these values into the Vergence Formula:
U + P = V
-1 + (-1) = V
-2 = V
V = -2D
-1 meter
P =
-1D
U = 1/-1m
= -1D

## Slide 31
U + P = V
-1D
Vergence: The Vergence Formula
-1 meter
Plugging these values into the Vergence Formula:
U + P = V
-1 + (-1) = V
-2 = V
1/-2 = -.5 meters
V = -2D
P =
-1D
U = 1/-1m
= -1D

## Slide 32
U + P = V
-1D
Vergence: The Vergence Formula
-1 meter
Plugging these values into the Vergence Formula:
U + P = V
-1 + (-1) = V
-2 = V
1/-2 = -.5 meters
Note that the cartoon seems to indicate that the
lens causes the rays to originate from this point.
This of course is not what happens. Nonetheless,
the lens does cause the exiting rays to diverge
as if they did! Weirder still, this point is considered
a focal point, even though the rays act as if they
are leaving, not approaching it. More shortly!
V = -2D
P =
-1D
U = 1/-1m
= -1D

## Slide 33
U = ?
U + P = V
-1D
Vergence: The Vergence Formula
To determine U, we need to know…
P =
-1D

## Slide 34
U = 1/+0.5 = +2D
U + P = V
-1D
Vergence: The Vergence Formula
+0.5 meters
To determine U, we need to know…this distance.
The vergence of converging
rays is always positive!
P =
-1D

## Slide 35
U = 1/+0.5 = +2D
U + P = V
-1D
Vergence: The Vergence Formula
+0.5 meters
Plugging these values into the Vergence Formula:
U + P = V
+2 + (-1) = V
+1 = V
Distance = 1/V = 1/1 = 1 meter
P =
-1D

## Slide 36
Vergence: The Vergence Formula
U + P = V
+4D
+3D
-0.5 m
Object
1 m
An object is located ½ m to the left of a +4D lens, which
is in turn 1 m to the left of a +3D lens. Where will the
final image be with respect to the second lens??
1 m to the right of the second lens. To solve vergence
problems such as this one, the key is to solve U+P=V
for the first lens, then treat the image thus produced as
the object for the next lens. This can be continued for any
number of lenses.

## Slide 37
Vergence: The Vergence Formula
U + P = V
+4D
+3D
-0.5 m
Object
1 m
An object is located ½ m to the left of a +4D lens, which
is in turn 1 m to the left of a +3D lens. Where will the
final image be with respect to the second lens??
1 m to the right of the second lens. To solve vergence
problems such as this one, the key is to solve U+P=V
for the first lens, then treat the image thus produced as
the object for the next lens. This can be continued for any
number of lenses.

## Slide 38
Vergence: The Vergence Formula
U + P = V
+4D
+3D
-0.5 m
1 m
For the +4D lens:
U = 1/-0.5 = -2D
P = +4
V = +2
The image from the first lens is 1/2
= .5 m to the right of the first lens
Object
An object is located ½ m to the left of a +4D lens, which
is in turn 1 m to the left of a +3D lens. Where will the
final image be with respect to the second lens??
1 m to the right of the second lens. To solve vergence
problems such as this one, the key is to solve U+P=V
for the first lens, then treat the image thus produced as
the object for the next lens. This can be continued for any
number of lenses.

## Slide 39
Vergence: The Vergence Formula
U + P = V
+4D
+3D
-0.5 m
1 m
For the +4D lens:
U = 1/-0.5 = -2D
P = +4D
V = +2
The image from the first lens is 1/2
= .5 m to the right of the first lens
Object
An object is located ½ m to the left of a +4D lens, which
is in turn 1 m to the left of a +3D lens. Where will the
final image be with respect to the second lens??
1 m to the right of the second lens. To solve vergence
problems such as this one, the key is to solve U+P=V
for the first lens, then treat the image thus produced as
the object for the next lens. This can be continued for any
number of lenses.

## Slide 40
Vergence: The Vergence Formula
U + P = V
+4D
+3D
-0.5 m
1 m
For the +4D lens:
U = 1/-0.5 = -2D
P = +4D
V = -2 + (+4) = +2D
The image from the first lens is 1/2
= .5 m to the right of the first lens
Object
An object is located ½ m to the left of a +4D lens, which
is in turn 1 m to the left of a +3D lens. Where will the
final image be with respect to the second lens??
1 m to the right of the second lens. To solve vergence
problems such as this one, the key is to solve U+P=V
for the first lens, then treat the image thus produced as
the object for the next lens. This can be continued for any
number of lenses.

## Slide 41
Vergence: The Vergence Formula
U + P = V
+4D
+3D
-0.5 m
1 m
For the +4D lens:
U = 1/-0.5 = -2D
P = +4D
V = -2 + (+4) = +2D
The image from the first lens is 1/2
= .5 m to the right of the first lens
Object
Image
0.5 m
An object is located ½ m to the left of a +4D lens, which
is in turn 1 m to the left of a +3D lens. Where will the
final image be with respect to the second lens??
1 m to the right of the second lens. To solve vergence
problems such as this one, the key is to solve U+P=V
for the first lens, then treat the image thus produced as
the object for the next lens. This can be continued for any
number of lenses.

## Slide 42
Vergence: The Vergence Formula
U + P = V
+4D
+3D
-0.5 m
1 m
Object
Image
0.5 m
For the +3D lens:
U = 1/-0.5 = -2D
P = +3
V = +1
The image formed by the second lens is 1/1
= 1 m to the right of the second lens
Object
-0.5 m
For the +4D lens:
U = 1/-0.5 = -2D
P = +4D
V = -2 + (+4) = +2D
The image from the first lens is 1/2
= .5 m to the right of the first lens
An object is located ½ m to the left of a +4D lens, which
is in turn 1 m to the left of a +3D lens. Where will the
final image be with respect to the second lens??
1 m to the right of the second lens. To solve vergence
problems such as this one, the key is to solve U+P=V
for the first lens, then treat the image thus produced as
the object for the next lens. This can be continued for any
number of lenses.

## Slide 43
Vergence: The Vergence Formula
U + P = V
+4D
+3D
-0.5 m
1 m
Object
Image
0.5 m
For the +3D lens:
U = 1/-0.5 = -2D
P = +3D
V = +1
The image formed by the second lens is 1/1
= 1 m to the right of the second lens
-0.5 m
For the +4D lens:
U = 1/-0.5 = -2D
P = +4D
V = -2 + (+4) = +2D
The image from the first lens is 1/2
= .5 m to the right of the first lens
An object is located ½ m to the left of a +4D lens, which
is in turn 1 m to the left of a +3D lens. Where will the
final image be with respect to the second lens??
1 m to the right of the second lens. To solve vergence
problems such as this one, the key is to solve U+P=V
for the first lens, then treat the image thus produced as
the object for the next lens. This can be continued for any
number of lenses.
Object

## Slide 44
Vergence: The Vergence Formula
U + P = V
+4D
+3D
-0.5 m
1 m
Object
Image
0.5 m
For the +3D lens:
U = 1/-0.5 = -2D
P = +3D
V = -2 + (+3) = +1D
The image formed by the second lens is 1/1
= 1 m to the right of the second lens
-0.5 m
For the +4D lens:
U = 1/-0.5 = -2D
P = +4D
V = -2 + (+4) = +2D
The image from the first lens is 1/2
= .5 m to the right of the first lens
An object is located ½ m to the left of a +4D lens, which
is in turn 1 m to the left of a +3D lens. Where will the
final image be with respect to the second lens??
1 m to the right of the second lens. To solve vergence
problems such as this one, the key is to solve U+P=V
for the first lens, then treat the image thus produced as
the object for the next lens. This can be continued for any
number of lenses.
Object

## Slide 45
Vergence: The Vergence Formula
U + P = V
+4D
+3D
-0.5 m
1 m
An object is located ½ m to the left of a +4D lens, which
is in turn 1 m to the left of a +3D lens. Where will the
final image be with respect to the second lens??
1 m to the right of the second lens. To solve vergence
problems such as this one, the key is to solve U+P=V
for the first lens, then treat the image thus produced as
the object for the next lens. This can be continued for any
number of lenses.
Object
Image
0.5 m
For the +3D lens:
U = 1/-0.5 = -2D
P = +3D
V = -2 + (+3) = +1D
The image formed by the second lens is 1/1
= 1 m to the right of the second lens
-0.5 m
1 m
Image
For the +4D lens:
U = 1/-0.5 = -2D
P = +4D
V = -2 + (+4) = +2D
The image from the first lens is 1/2
= .5 m to the right of the first lens
Object

## Slide 46
Vergence: The Vergence Formula
U + P = V
-2D
+1D
1 m
An object is located ½ m to the left of a -2D lens,
which is in turn 1 m to the left of a +1D lens. How far
is the final image from the object?
Object
-0.5 m

## Slide 47
Vergence: The Vergence Formula
U + P = V
-2D
+1D
1 m
For the -2D lens:
U = 1/-0.5 = -2D
Object
-0.5 m
An object is located ½ m to the left of a -2D lens,
which is in turn 1 m to the left of a +1D lens. How far
is the final image from the object?
6.50 m.

## Slide 48
Vergence: The Vergence Formula
U + P = V
-2D
+1D
1 m
For the -2D lens:
U = 1/-0.5 = -2D
P = -2D
Object
-0.5 m
An object is located ½ m to the left of a -2D lens,
which is in turn 1 m to the left of a +1D lens. How far
is the final image from the object?
6.50 m.

## Slide 49
Vergence: The Vergence Formula
U + P = V
-2D
+1D
1 m
For the -2D lens:
U = 1/-0.5 = -2D
P = -2D
V = -2 + (-2) = -4D
Object
-0.5 m
An object is located ½ m to the left of a -2D lens,
which is in turn 1 m to the left of a +1D lens. How far
is the final image from the object?
6.50 m.

## Slide 50
Vergence: The Vergence Formula
U + P = V
-2D
+1D
1 m
For the -2D lens:
U = 1/-0.5 = -2D
P = -2D
V = -2 + (-2) = -4D
The image from the first lens is 1/-4
= .25 m to the left of the first lens
Object
Image
-0.5 m
-.25 m
An object is located ½ m to the left of a -2D lens,
which is in turn 1 m to the left of a +1D lens. How far
is the final image from the object?
6.50 m.

## Slide 51
Vergence: The Vergence Formula
U + P = V
-2D
+1D
1 m
For the -2D lens:
U = 1/-0.5 = -2D
P = -2D
V = -4D
The image from the first lens is 1/-4
= .25 m to the left of the first lens
Object
Image
For the +1D lens:
U = 1/-1.25 m = -0.8D
P = +1
V = +0.2
The image formed by the second lens is
1/+0.2 = 5 m to the right of the second lens
Object
-1.25 m
-.25 m
An object is located ½ m to the left of a -2D lens,
which is in turn 1 m to the left of a +1D lens. How far
is the final image from the object?
6.50 m.
-0.5 m

## Slide 52
Vergence: The Vergence Formula
U + P = V
-2D
+1D
1 m
For the -2D lens:
U = 1/-0.5 = -2D
P = -2D
V = -4D
The image from the first lens is 1/-4
= .25 m to the left of the first lens
Object
Image
For the +1D lens:
U = 1/-1.25 m = -0.8D
P = +1D
V = +0.2
The image formed by the second lens is
1/+0.2 = 5 m to the right of the second lens
-1.25 m
-.25 m
An object is located ½ m to the left of a -2D lens,
which is in turn 1 m to the left of a +1D lens. How far
is the final image from the object?
6.50 m.
-0.5 m
Object

## Slide 53
Vergence: The Vergence Formula
U + P = V
-2D
+1D
1 m
For the -2D lens:
U = 1/-0.5 = -2D
P = -2D
V = -4D
The image from the first lens is 1/-4
= .25 m to the left of the first lens
Object
Image
For the +1D lens:
U = 1/-1.25 m = -0.8D
P = +1D
V = -0.8 + (+1) = +0.2D
The image formed by the second lens is
1/+0.2 = 5 m to the right of the second lens
-1.25 m
-.25 m
An object is located ½ m to the left of a -2D lens,
which is in turn 1 m to the left of a +1D lens. How far
is the final image from the object?
6.50 m.
-0.5 m
Object

## Slide 54
Vergence: The Vergence Formula
U + P = V
-2D
+1D
1 m
For the -2D lens:
U = 1/-0.5 = -2D
P = -2D
V = -4D
The image from the first lens is 1/-4
= .25 m to the left of the first lens
Object
Image
For the +1D lens:
U = 1/-1.25 m = -0.8D
P = +1D
V = -0.8 + (+1) = +0.2D
The image formed by the second lens is
1/+0.2 = 5 m to the right of the second lens
5 m
Image
-1.25 m
-.25 m
An object is located ½ m to the left of a -2D lens,
which is in turn 1 m to the left of a +1D lens. How far
is the final image from the object?
6.50 m.
-0.5 m
Object

## Slide 55
Vergence: The Vergence Formula
U + P = V
-2D
+1D
1 m
For the -2D lens:
U = 1/-0.5 = -2D
P = -2D
V = -4D
The image from the first lens is 1/-4
= .25 m to the left of the first lens
Object
Image
For the +1D lens:
U = 1/-1.25 m = -0.8D
P = +1D
V = -0.8 + (+1) = +0.2D
The image formed by the second lens is
1/+0.2 = 5 m to the right of the second lens
5 m
Image
-1.25 m
-.25 m
6.50 m
Distance from object
to image = 6.50 m
An object is located ½ m to the left of a -2D lens,
which is in turn 1 m to the left of a +1D lens. How far
is the final image from the object?
6.50 m
-0.5 m
Object

## Slide 56
Vergence: The Vergence Formula
U + P = V
-2D
+1D
1 m
For the -2D lens:
U = 1/-0.5 = -2
P = -2
V = -4
The image from the first lens is 1/-4
= .25 m to the left of the first lens
Object
Image
For the +1D lens:
U = 1/-1.25 m = -0.8
P = +1
V = +0.2
The image from the second lens is 1/+0.2
= 5 m to the right of the second lens
5 m
Image
-1.25 m
-.25 m
6.50 m
Distance from object
to image = 6.50 m
An object is located ½ m to the left of a -2D lens,
which is in turn 1 m to the left of a +1D lens. How far
is the final image from the object?
6.50 m
-0.5 m
But it looks like the rays from the first image/second object have to pass through the -2D lens
twice before reaching the +1D lens. Doesn’t this refract those rays again?
NO. After the light bouncing off the physical object passes through the -2D lens, it acts as if it
came from the first image/second object location, but it’s not really coming from there. In fact,
as we will come to see, clinical optics is less a description of what light actually does than it is
a powerful metaphor that allows us to make useful descriptions (and prescriptions!) of what
light does. In essence, clinical optics is a convenient fiction. More on this (much) later.
First pass through the lens
Second pass through the lens?
Object

## Slide 57
Vergence: The Vergence Formula
U + P = V
-2D
+1D
1 m
For the -2D lens:
U = 1/-0.5 = -2
P = -2
V = -4
The image from the first lens is 1/-4
= .25 m to the left of the first lens
Object
Image
For the +1D lens:
U = 1/-1.25 m = -0.8
P = +1
V = +0.2
The image from the second lens is 1/+0.2
= 5 m to the right of the second lens
5 m
Image
-1.25 m
-.25 m
6.50 m
Distance from object
to image = 6.50 m
An object is located ½ m to the left of a -2D lens,
which is in turn 1 m to the left of a +1D lens. How far
is the final image from the object?
6.50 m
-0.5 m
But it looks like the rays from the first image/second object have to pass through the -2D lens
twice before reaching the +1D lens. Doesn’t this refract those rays again?
NO. After the light bouncing off the physical object passes through the -2D lens, it acts as if it
came from the first image/second object location, but it’s not really coming from there. In fact,
as we will come to see, clinical optics is less a description of what light actually does than it is
a powerful metaphor that allows us to make useful descriptions (and prescriptions!) of what
light does. In essence, clinical optics is a convenient fiction. More on this (much) later.
Object

## Slide 58
Vergence: The Vergence Formula
U + P = V
-2D
+1D
1 m
For the -2D lens:
U = 1/-0.5 = -2D
P = -2D
V = -4D
The image from the first lens is 1/-4
= .25 m to the left of the first lens
Object
Image
For the +1D lens:
U = 1/-1.25 m = -0.8D
P = +1D
V = +0.2D
The image from the second lens is 1/+0.2
= 5 m to the right of the second lens
5 m
Image
-1.25 m
-.25 m
6.50 m
Distance from object
to image = 6.50 m
An object is located ½ m to the left of a -2D lens,
which is in turn 1 m to the left of a +1D lens. How far
is the final image from the object?
6.50 m.
-0.5 m
OK, but there’s another problem. Clearly, the rays that have passed through
the -2D are far too divergent to pass through the +1D lens—they’re going to
miss it by a mile! How can these rays possibly be refracted by the second lens?
Don’t let such ‘drawing artifacts’ fool you—some of the light will make it through
the second lens.
Object

## Slide 59
Vergence: The Vergence Formula
U + P = V
-2D
+1D
1 m
For the -2D lens:
U = 1/-0.5 = -2D
P = -2D
V = -4D
The image from the first lens is 1/-4
= .25 m to the left of the first lens
Object
Image
For the +1D lens:
U = 1/-1.25 m = -0.8D
P = +1D
V = +0.2D
The image from the second lens is 1/+0.2
= 5 m to the right of the second lens
5 m
Image
-1.25 m
-.25 m
6.50 m
Distance from object
to image = 6.50 m
An object is located ½ m to the left of a -2D lens,
which is in turn 1 m to the left of a +1D lens. How far
is the final image from the object?
6.50 m.
-0.5 m
OK, but there’s another problem. Clearly, the rays that have passed through
the -2D are far too divergent to pass through the +1D lens—they’re going to
miss it by a mile! How can these rays possibly be refracted by the second lens?
Don’t let such ‘drawing artifacts’ fool you—some of the light will make it through
the second lens.
Object

## Slide 60
Vergence: The Vergence Formula
U + P = V
-2D
+1D
1 m
For the -2D lens:
U = 1/-0.5 = -2
P = -2D
V = -4D
The image from the first lens is 1/-4
= .25 m to the left of the first lens
Object
Image
For the +1D lens:
U = 1/-1.25 m = -0.8D
P = +1D
V = +0.2D
The image from the second lens is 1/+0.2
= 5 m to the right of the second lens
5 m
Image
-1.25 m
-.25 m
6.50 m
Distance from object
to image = 6.50 m
An object is located ½ m to the left of a -2D lens,
which is in turn 1 m to the left of a +1D lens. How far
is the final image from the object?
6.50 m.
-0.5 m
OK, but there’s another problem. Clearly, the rays that have passed through
the -2D are far too divergent to pass through the +1D lens—they’re going to
miss it by a mile. How can these rays possibly be refracted by the second lens?
Don’t let such ‘drawing artifacts’ fool you—some of the light will make it through
the second lens.
In fact, to make this point explicitly, illustrators will
sometimes use dashed lines to ‘extend’ a lens so
as to capture the rays in question.
Object

## Slide 61
Vergence: The Vergence Formula
1D
1 meter
The ability of a lens to induce vergence is expressed in diopters
  Dioptric power of a lens: The reciprocal of the distance (in meters) to the point where incoming parallel light rays would intersect after passing through the lens
We encountered this slide a few minutes ago…
The notion that a diopter does something to light over the course of a meter
should remind you of the effect a prism has on light…

## Slide 62
Vergence: The Vergence Formula
1 meter
1 cm
1D
1 meter
1 PD
(Obviously
not to scale)
A prism diopter (PD, or D) displaces light 1 cm at 1 meter.

## Slide 63
Vergence: The Vergence Formula
1 meter
1 cm
1D
1 meter
1 PD
A prism diopter (PD, or D) displaces light 1 cm at 1 meter.
(Obviously
not to scale)
Which do prisms induce:
convergence or divergence?
Neither--prisms do not induce
vergence! Prisms cause light
rays to change direction, but
not to converge or diverge.

## Slide 64
Vergence: The Vergence Formula
1 meter
1 cm
1D
1 meter
1 PD
A prism diopter (PD, or D) displaces light 1 cm at 1 meter.
(Obviously
not to scale)
Which do prisms induce:
convergence or divergence?
Neither--prisms do not induce
vergence! Prisms cause light
rays to change direction, but
not to converge or diverge.

## Slide 65
Vergence: The Vergence Formula
1 meter
1D
1 meter
1 PD
1 cm
(Obviously
not to scale)
But, if we placed two prisms
base-to-base or apex-to-apex,
we could get light to converge
and diverge, respectively

## Slide 66
Vergence: The Vergence Formula
1 meter
1D
1 meter
=
=
1 PD
1 cm
(Obviously
not to scale)
In fact, we will at times find it very
useful to think of lenses as being
composed of prisms arranged in
just this manner!

## Slide 67
Of course, prisms also disperse white light into its component colors. They do
this because the different wavelengths are refracted different amounts. And
because they are composed of prisms… lenses do too.
Vergence: The Vergence Formula

## Slide 68
Of course, prisms also disperse white light into its component colors. They do
this because the different wavelengths are refracted different amounts. And
because they are composed of prisms…lenses do too.
Vergence: The Vergence Formula

## Slide 69
Vergence: The Vergence Formula
As we shall see in a
later chapter, this property
accounts for an important ocular phenomenon called chromatic aberration.