## Slide 1: Aberrations
Aberrations are phenomena that degrade the quality of the image formed by an optical system

## Slide 2: Aberrations
Aberrations are phenomena that degrade the quality of the image formed by an optical system
Degradation results when light rays from a given object-point fail to form a single sharp image

## Slide 3: Aberrations
Aberrations are phenomena that degrade the quality of the image formed by an optical system
Degradation results when light rays from a given object-point fail to form a single image-point

## Slide 4: Aberrations
Aberrations are phenomena that degrade the quality of the image formed by an optical system
Degradation results when light rays from a given object-point fail to form a single image-point
It’s important to recognize that aberrations are the rule, not the exception
  Aberration-free vision essentially never occurs

## Slide 5: Aberrations
Some aberrations are attributable to corrective lenses

## Slide 6: Aberrations
Some aberrations are attributable to corrective lenses
Others are intrinsic to the eye itself

## Slide 7: Aberrations
Some aberrations are attributable to corrective lenses
Others are intrinsic to the eye itself
  Three familiar forms:
    Spherical error (myopia/hyperopia)
    Cylinder (astigmatism)
    Chromatic aberration

## Slide 8: Aberrations
Some aberrations are attributable to corrective lenses
Others are intrinsic to the eye itself
  Three familiar forms:
    Spherical error (myopia/hyperopia)
    Cylinder (astigmatism)
    Chromatic aberration

## Slide 9
Aberrations
Back in the day, only three aberrations were addressed by clinicians:
  1) Spherical error (ie, myopia/hyperopia)
  2) Regular astigmatism
    Regular meaning ‘that which can be corrected with cylindrical lenses’
  3) Irregular astigmatism
    Irregular meaning ‘that which can’t be corrected with cylindrical lenses’

## Slide 10
Aberrations
Back in the day, only three aberrations were addressed by clinicians:
  1) Spherical error (ie, myopia/hyperopia)
  2) Regular astigmatism
    Regular meaning ‘that which can be corrected with cylindrical lenses’
  3) Irregular astigmatism
    Irregular meaning ‘that which can’t be corrected with cylindrical lenses’

## Slide 11
Aberrations
Back in the day, only three aberrations were addressed by clinicians:
  1) Spherical error (ie, myopia/hyperopia)
  2) Regular astigmatism
    Regular meaning ‘that which can be corrected with cylindrical lenses’
  3) Irregular astigmatism
    Irregular meaning ‘that which can’t be corrected with cylindrical lenses’

## Slide 12
Aberrations
Back in the day, only three aberrations were addressed by clinicians:
  1) Spherical error (ie, myopia/hyperopia)
  2) Regular astigmatism
    Regular meaning ‘that which can be corrected with cylindrical lenses’
  3) Irregular astigmatism
    Irregular meaning ‘that which can’t be corrected with cylindrical lenses’

## Slide 13
Aberrations
Back in the day, only three aberrations were addressed by clinicians:
  1) Spherical error (ie, myopia/hyperopia)
  2) Regular astigmatism
    Regular meaning ‘that which can be corrected with cylindrical lenses’
  3) Irregular astigmatism
    Irregular meaning ‘that which can’t be corrected with cylindrical lenses’

## Slide 14
Aberrations
Back in the day, only three aberrations were addressed by clinicians:
  1) Spherical error (ie, myopia/hyperopia)
  2) Regular astigmatism
    Regular meaning ‘that which can be corrected with cylindrical lenses’
  3) Irregular astigmatism
    Irregular meaning ‘that which can’t be corrected with cylindrical lenses’

## Slide 15
Aberrations
Back in the day, only three aberrations were addressed by clinicians:
  1) Spherical error (ie, myopia/hyperopia)
  2) Regular astigmatism
    Regular meaning ‘that which can be corrected with cylindrical lenses’
  3) Irregular astigmatism
    Irregular meaning ‘that which can’t be corrected with cylindrical lenses’
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected (by glasses) even if they had been measureable

## Slide 16
Aberrations
Sphere
Cylinder
‘Regular
Astigmatism’
‘Irregular
Astigmatism’
Old Lingo
Myopia
Hyperopia
Any component
of refractive error
that could not be
remediated with
spherical and/or
cylindrical lenses
This is how we thought of aberrations back in the day

## Slide 17
Aberrations
Wavefront analysis did away with the first problem
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected even if they had been measureable
two words

## Slide 18
Wavefront analysis did away with the first problem
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected even if they had been measureable
Aberrations: Wavefront Analysis

## Slide 19
Wavefront analysis did away with the first problem
  Allows clinicians to identify/quantify many of the refractive problems previously consigned to the irregular-astigmatism wastebasket
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected even if they had been measureable
Aberrations: Wavefront Analysis

## Slide 20
Wavefront analysis did away with the first problem
  Allows clinicians to identify/quantify many of the refractive problems previously consigned to the irregular-astigmatism wastebasket
  Several different technologies for measuring the wavefront have been developed, but one dominates current clinical practice: The Hartmann-Shack wavefront sensor
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected even if they had been measureable
Aberrations: Wavefront Analysis

## Slide 21
Wavefront analysis did away with the first problem
  Allows clinicians to identify/quantify many of the refractive problems previously consigned to the irregular-astigmatism wastebasket
  Several different technologies for measuring the wavefront have been developed, but one dominates current clinical practice: The Hartmann-Shack wavefront sensor
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected even if they had been measureable
Aberrations: Wavefront Analysis

## Slide 22
Aberrations: Wavefront Analysis
Wavefront analysis did away with the first problem
  Allows clinicians to identify/quantify many of the refractive problems previously consigned to the irregular-astigmatism wastebasket
  Several different technologies for measuring the wavefront have been developed, but one dominates current clinical practice: The Hartmann-Shack wavefront sensor
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected even if they had been measureable
How does the Hartmann-Shack wavefront sensor (HSWS) work?
Essentially, by reversing the function of the eye. Instead of treating the eye as a light-gathering device, it treats the eye as a light-emitting device. It then analyzes the wavefront of light emitted by the eye with respect to how ‘pure’ (ie, how uniform and free of warpage) it is.
How does the HSWS turn the eye into a light-emitting device?
By firing a low-power laser at the fovea, which reflects off the fovea. This reflected light then passes through the focusing structures of the eye (ie, the lens and cornea, and leaves the eye.
OK, so the HSWS turns the eye into a flashlight of sorts. How does this allow for identification and quantification of aberrations?
The HSWS contains an array of sensors that measure the ‘emitted’ light. If the refracting structures of the eye were perfect (ie, aberration-free), the wavefront of the emitted light would be perfectly flat; any deviation from flatness represents aberration, which in turn reflects imperfections in the eye’s focusing structures.

## Slide 23
Aberrations: Wavefront Analysis
Wavefront analysis did away with the first problem
  Allows clinicians to identify/quantify many of the refractive problems previously consigned to the irregular-astigmatism wastebasket
  Several different technologies for measuring the wavefront have been developed, but one dominates current clinical practice: The Hartmann-Shack wavefront sensor
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected even if they had been measureable
How does the Hartmann-Shack wavefront sensor (HSWS) work?
Essentially, by reversing the function of the eye. Instead of treating the eye as a light-gathering device, it treats the eye as a light-emitting device. It then analyzes the wavefront of light emitted by the eye with respect to how ‘pure’ (ie, how uniform and free of warpage) it is.
How does the HSWS turn the eye into a light-emitting device?
By firing a low-power laser at the fovea, which reflects off the fovea. This reflected light then passes through the focusing structures of the eye (ie, the lens and cornea, and leaves the eye.
OK, so the HSWS turns the eye into a flashlight of sorts. How does this allow for identification and quantification of aberrations?
The HSWS contains an array of sensors that measure the ‘emitted’ light. If the refracting structures of the eye were perfect (ie, aberration-free), the wavefront of the emitted light would be perfectly flat; any deviation from flatness represents aberration, which in turn reflects imperfections in the eye’s focusing structures.

## Slide 24
Aberrations: Wavefront Analysis
Wavefront analysis did away with the first problem
  Allows clinicians to identify/quantify many of the refractive problems previously consigned to the irregular-astigmatism wastebasket
  Several different technologies for measuring the wavefront have been developed, but one dominates current clinical practice: The Hartmann-Shack wavefront sensor
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected even if they had been measureable
How does the Hartmann-Shack wavefront sensor (HSWS) work?
Essentially, by reversing the function of the eye. Instead of treating the eye as a light-gathering device, it treats the eye as a light-emitting device. It then analyzes the wavefront of light emitted by the eye with respect to how ‘pure’ (ie, how uniform and free of warpage) it is.
How does the HSWS turn the eye into a light-emitting device?
By firing a low-power laser at the fovea, which reflects off the fovea. This reflected light then passes through the focusing structures of the eye (ie, the lens and cornea, and leaves the eye.
OK, so the HSWS turns the eye into a flashlight of sorts. How does this allow for identification and quantification of aberrations?
The HSWS contains an array of sensors that measure the ‘emitted’ light. If the refracting structures of the eye were perfect (ie, aberration-free), the wavefront of the emitted light would be perfectly flat; any deviation from flatness represents aberration, which in turn reflects imperfections in the eye’s focusing structures.

## Slide 25
Aberrations: Wavefront Analysis
Wavefront analysis did away with the first problem
  Allows clinicians to identify/quantify many of the refractive problems previously consigned to the irregular-astigmatism wastebasket
  Several different technologies for measuring the wavefront have been developed, but one dominates current clinical practice: The Hartmann-Shack wavefront sensor
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected even if they had been measureable
How does the Hartmann-Shack wavefront sensor (HSWS) work?
Essentially, by reversing the function of the eye. Instead of treating the eye as a light-gathering device, it treats the eye as a light-emitting device. It then analyzes the wavefront of light emitted by the eye with respect to how ‘pure’ (ie, how uniform and free of warpage) it is.
How does the HSWS turn the eye into a light-emitting device?
By firing a low-power laser into the eye that reflects off the fovea. The reflected light then passes through the focusing structures of the eye (ie, the lens and cornea), and leaves the eye.
OK, so the HSWS turns the eye into a flashlight of sorts. How does this allow for identification and quantification of aberrations?
The HSWS contains an array of sensors that measure the ‘emitted’ light. If the refracting structures of the eye were perfect (ie, aberration-free), the wavefront of the emitted light would be perfectly flat; any deviation from flatness represents aberration, which in turn reflects imperfections in the eye’s focusing structures.

## Slide 26
Aberrations: Wavefront Analysis
Wavefront analysis did away with the first problem
  Allows clinicians to identify/quantify many of the refractive problems previously consigned to the irregular-astigmatism wastebasket
  Several different technologies for measuring the wavefront have been developed, but one dominates current clinical practice: The Hartmann-Shack wavefront sensor
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected even if they had been measureable
How does the Hartmann-Shack wavefront sensor (HSWS) work?
Essentially, by reversing the function of the eye. Instead of treating the eye as a light-gathering device, it treats the eye as a light-emitting device. It then analyzes the wavefront of light emitted by the eye with respect to how ‘pure’ (ie, how uniform and free of warpage) it is.
How does the HSWS turn the eye into a light-emitting device?
By firing a low-power laser into the eye that reflects off the fovea. The reflected light then passes through the focusing structures of the eye (ie, the lens and cornea), and leaves the eye.
OK, so the HSWS turns the eye into a flashlight of sorts. How does this allow for identification and quantification of aberrations?
The HSWS contains an array of sensors that measure the ‘emitted’ light. If the refracting structures of the eye were perfect (ie, aberration-free), the wavefront of the emitted light would be perfectly flat; any deviation from flatness represents aberration, which in turn reflects imperfections in the eye’s focusing structures.

## Slide 27
Aberrations: Wavefront Analysis
Wavefront analysis did away with the first problem
  Allows clinicians to identify/quantify many of the refractive problems previously consigned to the irregular-astigmatism wastebasket
  Several different technologies for measuring the wavefront have been developed, but one dominates current clinical practice: The Hartmann-Shack wavefront sensor
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected even if they had been measureable
How does the Hartmann-Shack wavefront sensor (HSWS) work?
Essentially, by reversing the function of the eye. Instead of treating the eye as a light-gathering device, it treats the eye as a light-emitting device. It then analyzes the wavefront of light emitted by the eye with respect to how ‘pure’ (ie, how uniform and free of warpage) it is.
How does the HSWS turn the eye into a light-emitting device?
By firing a low-power laser into the eye that reflects off the fovea. The reflected light then passes through the focusing structures of the eye (ie, the lens and cornea), and leaves the eye.
OK, so the HSWS turns the eye into a flashlight of sorts. How does this allow for identification and quantification of aberrations?
The HSWS contains an array of sensors that measure the ‘emitted’ light. If the refracting structures of the eye were perfect (ie, aberration-free), the wavefront of the emitted light would be perfectly flat--any deviation from flatness represents aberration, which in turn reflects imperfections in the eye’s focusing structures.

## Slide 28
Aberrations
Sphere
Cylinder
‘Regular
Astigmatism’
‘Irregular
Astigmatism’
Defocus
Old Lingo
New Lingo
=
Any component
of refractive error
that could not be
remediated with
spherical and/or
cylindrical lenses
Myopia
Hyperopia
(from wavefront analysis)

## Slide 29
Aberrations
Sphere
Cylinder
‘Regular
Astigmatism’
‘Irregular
Astigmatism’
Defocus
Old Lingo
New Lingo
=
Myopia
Hyperopia
Positive defocus
Negative defocus
=
=
Any component
of refractive error
that could not be
remediated with
spherical and/or
cylindrical lenses
(from wavefront analysis)
+ vs (-)
+ vs (-)

## Slide 30
Aberrations
Sphere
Cylinder
‘Regular
Astigmatism’
‘Irregular
Astigmatism’
Defocus
Old Lingo
New Lingo
=
Myopia
Hyperopia
Positive defocus
Negative defocus
=
=
Any component
of refractive error
that could not be
remediated with
spherical and/or
cylindrical lenses
(from wavefront analysis)
To remember which is which, note that each is the same as the error lens responsible for each status

## Slide 31
Aberrations
Sphere
Cylinder
‘Regular
Astigmatism’
‘Irregular
Astigmatism’
Defocus
Cylinder
Old Lingo
New Lingo
=
=
Myopia
Hyperopia
Positive defocus
Negative defocus
=
=
Any component
of refractive error
that could not be
remediated with
spherical and/or
cylindrical lenses
(from wavefront analysis)

## Slide 32
Aberrations
Sphere
Cylinder
‘Regular
Astigmatism’
‘Irregular
Astigmatism’
Defocus
Cylinder
Old Lingo
New Lingo
=
=
Myopia
Hyperopia
Positive defocus
Negative defocus
=
=
Any component
of refractive error
that could not be
remediated with
spherical and/or
cylindrical lenses
(from wavefront analysis)

## Slide 33
Aberrations
Sphere
Cylinder
‘Regular
Astigmatism’
‘Irregular
Astigmatism’
Defocus
Cylinder
Old Lingo
New Lingo
=
=
Myopia
Hyperopia
Positive defocus
Negative defocus
=
=
Any component
of refractive error
that could not be
remediated with
spherical and/or
cylindrical lenses
(from wavefront analysis)
‘Lower-order
Aberrations’

## Slide 34
Aberrations
Sphere
Cylinder
‘Regular
Astigmatism’
‘Irregular
Astigmatism’
Defocus
Cylinder
Old Lingo
New Lingo
Spherical
aberration
Coma
=
Trefoil
(Others, less
clinically relevant)
=
Myopia
Hyperopia
Positive defocus
Negative defocus
=
=
Any component
of refractive error
that could not be
remediated with
spherical and/or
cylindrical lenses
(from wavefront analysis)
=
‘Lower-order
Aberrations’
two words

## Slide 35
Aberrations
Sphere
Cylinder
‘Regular
Astigmatism’
‘Irregular
Astigmatism’
Defocus
Cylinder
Old Lingo
New Lingo
Spherical
aberration
Coma
=
Trefoil
(Others, less
clinically relevant)
=
Myopia
Hyperopia
Positive defocus
Negative defocus
=
=
Any component
of refractive error
that could not be
remediated with
spherical and/or
cylindrical lenses
(from wavefront analysis)
=
‘Lower-order
Aberrations’

## Slide 36
Aberrations
Sphere
Cylinder
‘Regular
Astigmatism’
‘Irregular
Astigmatism’
Defocus
Cylinder
Old Lingo
New Lingo
‘Lower-order
Aberrations’
‘Higher-order
Aberrations’
=
=
Myopia
Hyperopia
Positive defocus
Negative defocus
=
=
Any component
of refractive error
that could not be
remediated with
spherical and/or
cylindrical lenses
(from wavefront analysis)
Spherical
aberration
Coma
Trefoil
(Others, less
clinically relevant)
=

## Slide 37
Aberrations
Sphere
Cylinder
‘Regular
Astigmatism’
‘Irregular
Astigmatism’
Defocus
Cylinder
Old Lingo
New Lingo
‘Lower-order
Aberrations’
‘Higher-order
Aberrations’
=
=
Myopia
Hyperopia
Positive defocus
Negative defocus
=
=
Any component
of refractive error
that could not be
remediated with
spherical and/or
cylindrical lenses
(from wavefront analysis)
Spherical
aberration
Coma
Trefoil
(Others, less
clinically relevant)
=
We will address these in greater detail later in this slide-set

## Slide 38: Aberrations
Not paraxial (nearly parallel to optical axis, but not close to it)
Optical
axis
Paraxial rays
ni = 1.0 nt = 1.34
Not paraxial (close to optical axis, but not parallel to it)
When dealing with refraction at a curved surface, we work only with the paraxial rays:
Those that are both close to the optical axis and nearly parallel to it.
(The above was presented first in the slide-set Basic Optics, Chapter 17. If you have no idea what it’s about, consider reviewing that chapter.)

## Slide 39: Aberrations
Not paraxial (nearly parallel to optical axis, but not close to it)
Optical
axis
Paraxial rays
ni = 1.0 nt = 1.34
Not paraxial (close to optical axis, but not parallel to it)
When dealing with refraction at a curved surface, we work only with the paraxial rays:
Those that are both close to the optical axis and nearly parallel to it.
Until now, we have focused exclusively on the optics of paraxial rays. But to understand higher-order aberrations, we have to consider the optics of nonparaxial rays.

## Slide 40: Aberrations
Not paraxial (nearly parallel to optical axis, but not close to it)
Optical
axis
Paraxial rays
ni = 1.0 nt = 1.34
Not paraxial (close to optical axis, but not parallel to it)
When dealing with refraction at a curved surface, we work only with the paraxial rays:
Those that are both close to the optical axis and nearly parallel to it.
Until now, we have focused exclusively on the optics of paraxial rays. But to understand higher-order aberrations, we have to consider the optics of nonparaxial rays.
The clinically most important higher-order aberration stemming from nonparaxial rays is spherical aberration, so we’ll discuss it first.
two words

## Slide 41: Aberrations
Not paraxial (nearly parallel to optical axis, but not close to it)
Optical
axis
Paraxial rays
ni = 1.0 nt = 1.34
Not paraxial (close to optical axis, but not parallel to it)
When dealing with refraction at a curved surface, we work only with the paraxial rays:
Those that are both close to the optical axis and nearly parallel to it.
Until now, we have focused exclusively on the optics of paraxial rays. But to understand higher-order aberrations, we have to consider the optics of nonparaxial rays.
The clinically most important higher-order aberration stemming from nonparaxial rays is spherical aberration, so we’ll discuss it first.

## Slide 42
A spherical lens is one for which the refracting surface(s) have a single radius of curvature
Aberrations: Spherical
three words

## Slide 43
A spherical lens is one for which the refracting surface(s) have a single radius of curvature
Aberrations: Spherical

## Slide 44
A spherical lens is one for which the refracting surface(s) have a single radius of curvature
Note that a spherical lens need not be a sphere!
For a lens to be ‘spherical,’ its refracting surface(s)
must have a single radius-of-curvature—as if the
lens was sliced off of a sphere.
Spherical lens
Sphere
Aberrations: Spherical

## Slide 45
A spherical lens is one for which the refracting surface(s) have a single radius of curvature
Note that a spherical lens need not have a single
refracting surface.
Sphere
Spherical lens
Sphere
Aberrations: Spherical

## Slide 46
A spherical lens is one for which the refracting surface(s) have a single radius of curvature
Note that a spherical lens need not be a plus lens, either.
Spherical (minus) lens
Sphere-shaped
void in the glass
Minus
lens
cut
out
of
the
glass
Solid block of glass
Aberrations: Spherical

## Slide 47
A spherical lens is one for which the refracting surface(s) have a single radius of curvature
Aberrations: Spherical
spherocylindrical
^
What about the refracting surface of a spherocylindrical (S-C) lens?
Rhetorical question—advance when ready
Spherocylindrical lens?
Sphere

## Slide 48
A spherical lens is one for which the refracting surface(s) have a single radius of curvature
Aberrations: Spherical
spherocylindrical
^
What about the refracting surface of a spherocylindrical (S-C) lens?
Recall that, by definition, a S-C lens has two different powers oriented at right angles to one another. This means every point on its surface has two radii—one for each power.
two
i
Sphere
Spherocylindrical lens?

## Slide 49
A spherical lens is one for which the refracting surface(s) have a single radius of curvature
Aberrations: Spherical
spherocylindrical
^
What about the refracting surface of a spherocylindrical (S-C) lens?
Recall that, by definition, a S-C lens has two different powers oriented at right angles to one another. This means every point on its surface has two radii—one for each power. Thus, such a lens could not be created by slicing off a section from a sphere.
two
i
Sphere
Spherocylindrical lens?

## Slide 50
A spherical lens is one for which the refracting surface(s) have a single radius of curvature
Aberrations: Spherical
spherocylindrical
^
What about the refracting surface of a spherocylindrical (S-C) lens?
Recall that, by definition, a S-C lens has two different powers oriented at right angles to one another. This means every point on its surface has two radii—one for each power. Thus, such a lens could not be created by slicing off a section from a sphere.
Can you think of an everyday (hint: and delicious) object from which a slice could be taken that would qualify as a S-C lens?
two
i

## Slide 51
A spherical lens is one for which the refracting surface(s) have a single radius of curvature
Aberrations: Spherical
spherocylindrical
^
What about the refracting surface of a spherocylindrical (S-C) lens?
Recall that, by definition, a S-C lens has two different powers oriented at right angles to one another. This means every point on its surface has two radii—one for each power. Thus, such a lens could not be created by slicing off a section from a sphere.
Can you think of an everyday (hint: and delicious) object from which a slice could be taken that would qualify as a S-C lens?
Yes—a donut.
two
i

## Slide 52
A spherical lens is one for which the refracting surface(s) have a single radius of curvature
Aberrations: Spherical
spherocylindrical
^
What about the refracting surface of a spherocylindrical (S-C) lens?
Recall that, by definition, a S-C lens has two different powers oriented at right angles to one another. This means every point on its surface has two radii—one for each power. Thus, such a lens could not be created by slicing off a section from a sphere.
Can you think of an everyday (hint: and delicious) object from which a slice could be taken that would qualify as a S-C lens?
Yes—a donut. Every point on the surface of a donut has two radii—one determined by its distance from the center of the donut’s hole, the other by its distance from the center of the part you bite into.
two
i

## Slide 53
A spherical lens is one for which the refracting surface(s) have a single radius of curvature
Aberrations: Spherical
spherocylindrical
^
What about the refracting surface of a spherocylindrical (S-C) lens?
Recall that, by definition, a S-C lens has two different powers oriented at right angles to one another. This means every point on its surface has two radii—one for each power. Thus, such a lens could not be created by slicing off a section from a sphere.
Can you think of an everyday (hint: and delicious) object from which a slice could be taken that would qualify as a S-C lens?
Yes—a donut. Every point on the surface of a donut has two radii—one determined by its distance from the center of the donut’s hole, the other by its distance from the center of the part you bite into. So, just as a spherical lens is created by taking a slice off a sphere, a spherocylindrical lens is created by taking a slice off a donut.
two
i

## Slide 54
A spherical lens is one for which the refracting surface(s) have a single radius of curvature
Aberrations: Spherical
spherocylindrical
^
What about the refracting surface of a spherocylindrical (S-C) lens?
Recall that, by definition, a S-C lens has two different powers oriented at right angles to one another. This means every point on its surface has two radii—one for each power. Thus, such a lens could not be created by slicing off a section from a sphere.
Can you think of an everyday (hint: and delicious) object from which a slice could be taken that would qualify as an S-C lens?
Yes—a donut. Every point on the surface of a donut has two radii—one determined by its distance from the center of the donut’s hole; the other by its distance from the center of the part you bite into. So, just as a spherical lens is created by taking a slice off a sphere, a spherocylindrical lens is created by taking a slice off a donut.
two
i
There is a more formal/precise name for the shape from which a spherocylindrical lens is sliced—what is it?
A torus
Similarly, this more-formal name gives rise to an alternate name for a spherocylindrical lens—what is it?
A toric lens

## Slide 55
A spherical lens is one for which the refracting surface(s) have a single radius of curvature
Aberrations: Spherical
spherocylindrical
^
What about the refracting surface of a spherocylindrical (S-C) lens?
Recall that, by definition, a S-C lens has two different powers oriented at right angles to one another. This means every point on its surface has two radii—one for each power. Thus, such a lens could not be created by slicing off a section from a sphere.
Can you think of an everyday (hint: and delicious) object from which a slice could be taken that would qualify as an S-C lens?
Yes—a donut. Every point on the surface of a donut has two radii—one determined by its distance from the center of the donut’s hole; the other by its distance from the center of the part you bite into. So, just as a spherical lens is created by taking a slice off a sphere, a spherocylindrical lens is created by taking a slice off a donut.
two
i
There is a more formal/precise name for the shape from which a spherocylindrical lens is sliced—what is it?
A torus
Similarly, this more-formal name gives rise to an alternate name for a spherocylindrical lens—what is it?
A toric lens

## Slide 56
A spherical lens is one for which the refracting surface(s) have a single radius of curvature
Aberrations: Spherical
spherocylindrical
^
What about the refracting surface of a spherocylindrical (S-C) lens?
Recall that, by definition, a S-C lens has two different powers oriented at right angles to one another. This means every point on its surface has two radii—one for each power. Thus, such a lens could not be created by slicing off a section from a sphere.
Can you think of an everyday (hint: and delicious) object from which a slice could be taken that would qualify as an S-C lens?
Yes—a donut. Every point on the surface of a donut has two radii—one determined by its distance from the center of the donut’s hole; the other by its distance from the center of the part you bite into. So, just as a spherical lens is created by taking a slice off a sphere, a spherocylindrical lens is created by taking a slice off a donut.
two
i
There is a more formal/precise name for the shape from which a spherocylindrical lens is sliced—what is it?
A torus
Similarly, this more-formal name gives rise to an alternate name for a spherocylindrical lens—what is it?
A toric lens

## Slide 57
A spherical lens is one for which the refracting surface(s) have a single radius of curvature
Aberrations: Spherical
spherocylindrical
^
What about the refracting surface of a spherocylindrical (S-C) lens?
Recall that, by definition, a S-C lens has two different powers oriented at right angles to one another. This means every point on its surface has two radii—one for each power. Thus, such a lens could not be created by slicing off a section from a sphere.
Can you think of an everyday (hint: and delicious) object from which a slice could be taken that would qualify as an S-C lens?
Yes—a donut. Every point on the surface of a donut has two radii—one determined by its distance from the center of the donut’s hole; the other by its distance from the center of the part you bite into. So, just as a spherical lens is created by taking a slice off a sphere, a spherocylindrical lens is created by taking a slice off a donut.
two
i
There is a more formal/precise name for the shape from which a spherocylindrical lens is sliced—what is it?
A torus
Similarly, this more-formal name gives rise to an alternate name for a spherocylindrical lens—what is it?
A toric lens

## Slide 58
Aberrations: Spherical
Let’s drill down on how spherical aberration comes to pass:

## Slide 59
Object
point
Spherical lens
Consider an object-lens system as above.
Aberrations: Spherical
Let’s drill down on how spherical aberration comes to pass:

## Slide 60
Object
point
Image
point
Spherical lens
If we deal only with the paraxial rays, we find their focus closely approximates a
perfect point, as predicted by first-order optics.
Paraxial rays
Lens axis
Aberrations: Spherical
Let’s drill down on how spherical aberration comes to pass:

## Slide 61
However, when we look at the behavior of the non-paraxial rays, we find they do
not focus at the same location as the paraxial rays; rather, because they are more
sharply refracted, they focus anterior to the paraxial focal point.
Object
point
Spherical lens
If we deal only with the paraxial rays, we find their focus closely approximates a
perfect point, as predicted by first-order optics.
Lens axis
Nonparaxial rays
Nonparaxial rays
Paraxial rays
Aberrations: Spherical
Let’s drill down on how spherical aberration comes to pass:

## Slide 62
However, when we look at the behavior of the non-paraxial rays, we find they do
not focus at the same location as the paraxial rays; rather, because they are more
sharply refracted, they focus anterior to the paraxial focal point.
Object
point
Spherical lens
If we deal only with the paraxial rays, we find their focus closely approximates a
perfect point, as predicted by first-order optics.
Why are nonparaxial rays refracted more than paraxial rays on a spherical lens?
Recall that Snell’s Law states that the angle of refraction is a function of the angle of incidence. For paraxial rays, the angle of incidence is determined solely by the radius-of-curvature of the lens. However, the angle-of-incidence for non-paraxial rays is a function of both the radius of curvature and the fact that the surface of the lens becomes more and more oblique as you move away from the lens axis; ie, the lens periphery ‘turns away’ from the incoming light, thereby increasing the angle of incidence in a way unrelated to the radius of curvature.
Lens axis
Nonparaxial rays
Nonparaxial rays
Paraxial rays
Aberrations: Spherical

## Slide 63
However, when we look at the behavior of the non-paraxial rays, we find they do
not focus at the same location as the paraxial rays; rather, because they are more
sharply refracted, they focus anterior to the paraxial focal point.
Object
point
Spherical lens
If we deal only with the paraxial rays, we find their focus closely approximates a
perfect point, as predicted by first-order optics.
Why are nonparaxial rays refracted more than paraxial rays on a spherical lens?
Snell’s Law states that the angle of refraction is a function of the angle of incidence. For paraxial rays, the angle of incidence is determined solely by the radius-of-curvature of the lens. However, the angle-of-incidence for non-paraxial rays is a function of both the radius of curvature and the fact that the surface of the lens becomes more and more oblique (relative to the path of the light) as you move away from the lens axis; ie, the lens periphery ‘turns away’ from the incoming light, thereby increasing the angle of incidence in a way unrelated to the radius of curvature.
Lens axis
Nonparaxial rays
Nonparaxial rays
Paraxial rays
Aberrations: Spherical

## Slide 64
However, when we look at the behavior of the non-paraxial rays, we find they do
not focus at the same location as the paraxial rays; rather, because they are more
sharply refracted, they focus anterior to the paraxial focal point.
Object
point
Spherical lens
If we deal only with the paraxial rays, we find their focus closely approximates a
perfect point, as predicted by first-order optics.
Why are nonparaxial rays refracted more than paraxial rays on a spherical lens?
Snell’s Law states that the angle of refraction is a function of the angle of incidence. For paraxial rays, the angle of incidence is determined solely by the radius-of-curvature of the lens. However, the angle-of-incidence for non-paraxial rays is a function of both the radius of curvature and the fact that the surface of the lens becomes more and more oblique (relative to the path of the light) as you move away from the lens axis; ie, the lens periphery ‘turns away’ from the incoming light, thereby increasing the angle of incidence in a way unrelated to the radius of curvature.
Lens axis
Nonparaxial rays
Nonparaxial rays
Paraxial rays
Aberrations: Spherical

## Slide 65
However, when we look at the behavior of the non-paraxial rays, we find they do
not focus at the same location as the paraxial rays; rather, because they are more
sharply refracted, they focus anterior to the paraxial focal point. By the time these rays
reach the focal plane for the paraxial rays, they are diverging. Thus, they contribute
not to a focal point, but rather to a somewhat defocused area called a blur circle.
Object
point
Spherical lens
If we deal only with the paraxial rays, we find their focus closely approximates a
perfect point, as predicted by first-order optics.
Image
(blur circle)
Lens axis
Nonparaxial rays
Nonparaxial rays
Paraxial rays
Aberrations: Spherical

## Slide 66
However, when we look at the behavior of the non-paraxial rays, we find they do
not focus at the same location as the paraxial rays; rather, because they are more
sharply refracted, they focus anterior to the paraxial focal point. By the time these rays
reach the focal plane for the paraxial rays, they are diverging. Thus, they contribute
not to a focal point, but rather to a somewhat defocused area called a blur circle.
Object
point
Spherical lens
If we deal only with the paraxial rays, we find their focus closely approximates a
perfect point, as predicted by first-order optics.
When progressively peripheral rays are refracted more and more sharply,
the lens is said to possess positive spherical aberration.
Image
(blur circle)
Lens axis
Nonparaxial rays
Nonparaxial rays
Paraxial rays
Aberrations: Spherical

## Slide 67
However, when we look at the behavior of the non-paraxial rays, we find they do
not focus at the same location as the paraxial rays; rather, because they are more
sharply refracted, they focus anterior to the paraxial focal point.
Object
point
Spherical lens
If we deal only with the paraxial rays, we find their focus closely approximates a
perfect point, as predicted by first-order optics.
less
posterior
On the other hand, when progressively peripheral rays are refracted less
and less sharply, the lens is said to possess negative spherical aberration.
Image
(blur circle)
Non
Lens axis
Nonparaxial rays
Nonparaxial rays
Paraxial rays
-
Aberrations: Spherical

## Slide 68
Lens
axis
(All these rays
are from the
same
point
on the object
at infinity.)
Lens
axis
Aberrations: Spherical

## Slide 69
(All these rays
are from the
same
point
on the object
at infinity.)
Because of spherical
aberration, an optical
interval is produced
in which rays from
different ‘zones’ of the
lens are focused, but
all others aren’t.
Lens
axis
Lens
axis
Aberrations: Spherical

## Slide 70
Aberrations: Spherical
(All these rays
are from the
same
point
on the object
at infinity.)
A viewing screen placed
anywhere within this
interval would yield a
crisp image (due to rays
passing through one
zone of the lens), with
surrounding ‘halos’
representing rays from
the other zones (and
therefore out-of-focus
at this point in the interval)
Lens
axis
Lens
axis

## Slide 71
(All these rays
are from the
same
point
on the object
at infinity.)
And because it is an optical instrument…
Lens
axis
Lens
axis
Aberrations: Spherical

## Slide 72
(All these rays
are from the
same
point
on the object
at infinity.)
And because it is an optical instrument…the eye is subject to the same phenomenon.
Optical
axis
Optical
axis
Aberrations: Spherical

## Slide 73
Object
point
Image
point
Sharply-focused
retinal image point
When the pupil is small, light reaching the retina consists largely of paraxial rays; ie, rays passing through the
central portion of the cornea.
(Remember,
all these rays
are from the
same point
on the object
at infinity.)
Aberrations: Spherical

## Slide 74
Object
point
Image
blur circle
Poorly-focused
retinal blur circle
Note the myopic shift--
ie, peripheral rays are
focused in the vitreous
(Remember,
all these rays
are from the
same point
on the object
at infinity.)
When the pupil is small, light reaching the retina consists largely of paraxial rays; ie, rays passing through the
central portion of the cornea. However, when the pupil is large, rays passing through the peripheral
cornea come into play, and spherical aberration causes these rays to be focused more anteriorly, resulting
in a myopic component to the final image.
Aberrations: Spherical

## Slide 75
Object
point
Image
blur circle
Poorly-focused
retinal blur circle
Note the myopic shift--
ie, peripheral rays are
focused in the vitreous
(Remember,
all these rays
are from the
same point
on the object
at infinity.)
When the pupil is small, light reaching the retina consists largely of paraxial rays; ie, rays passing through the
central portion of the cornea. However, when the pupil is large, rays passing through the peripheral
cornea come into play, and spherical aberration causes these rays to be focused more anteriorly, resulting
in a myopic component to the final image. Spherical aberration is a factor in the phenomenon called night myopia, in which pts complain of blurred vision brought on by dusk- and night-time illumination levels.
Aberrations: Spherical

## Slide 76
(All these rays
are from the
same
point
on the object
at infinity.)
Optical
axis
Optical
axis
How much spherical aberration does the average human cornea possess?
About +0.27 mm (Why mm? Don’t ask.)
So this means the cornea possesses positive spherical aberration. But the cornea’s Q factor is negative. What gives?
The Q factor measures the relative asphericity of the cornea. A negative Q factor simply means the corneal periphery has less power than the central cornea; it does not mean the cornea as a whole doesn’t have spherical aberration!
Aberrations: Spherical

## Slide 77
(All these rays
are from the
same
point
on the object
at infinity.)
Optical
axis
Optical
axis
How much spherical aberration does the average human cornea possess?
About +0.27 mm
So this means the cornea possesses positive spherical aberration. But the cornea’s Q factor is negative. What gives?
The Q factor measures the relative asphericity of the cornea. A negative Q factor simply means the corneal periphery has less power than the central cornea; it does not mean the cornea as a whole doesn’t have spherical aberration!
Aberrations: Spherical

## Slide 78
Aberrations: Spherical
(All these rays
are from the
same
point
on the object
at infinity.)
Optical
axis
Optical
axis
How much spherical aberration does the average human cornea possess?
About +0.27 mm
So this means the cornea possesses positive spherical aberration. But the cornea’s Q factor is negative. What gives?
The Q factor measures the relative asphericity of the cornea. A negative Q factor simply means the corneal periphery has less power than the central cornea; it does not mean the cornea as a whole doesn’t have spherical aberration!
Why is the unit of spherical aberration microns--a unit of distance? What distance is being referred to?
It refers to the distance between the location where central rays for a focal point and where the peripheral rays form a focal point
But as can be seen in the figure, the location of the focal point for rays passing through the corneal periphery is a function of ‘how peripheral’ those rays are. Given this, how can one measure spherical aberration?
By convention, rays passing through the cornea 6 mm from the optical axis are used

## Slide 79
Aberrations: Spherical
(All these rays
are from the
same
point
on the object
at infinity.)
Optical
axis
Optical
axis
How much spherical aberration does the average human cornea possess?
About +0.27 mm
So this means the cornea possesses positive spherical aberration. But the cornea’s Q factor is negative. What gives?
The Q factor measures the relative asphericity of the cornea. A negative Q factor simply means the corneal periphery has less power than the central cornea; it does not mean the cornea as a whole doesn’t have spherical aberration!
Why is the unit of spherical aberration microns--a unit of distance? What distance is being referred to?
It refers to the distance between the location where central rays form a focal point and where the peripheral rays form a focal point
But as can be seen in the figure, the location of the focal point for rays passing through the corneal periphery is a function of ‘how peripheral’ those rays are. Given this, how can one measure spherical aberration?
By convention, rays passing through the cornea 6 mm from the optical axis are used

## Slide 80
Aberrations: Spherical
(All these rays
are from the
same
point
on the object
at infinity.)
Optical
axis
Optical
axis
How much spherical aberration does the average human cornea possess?
About +0.27 mm
So this means the cornea possesses positive spherical aberration. But the cornea’s Q factor is negative. What gives?
The Q factor measures the relative asphericity of the cornea. A negative Q factor simply means the corneal periphery has less power than the central cornea; it does not mean the cornea as a whole doesn’t have spherical aberration!
Why is the unit of spherical aberration microns--a unit of distance? What distance is being referred to?
It refers to the distance between the location where central rays form a focal point and where the peripheral rays form a focal point
But as can be seen in the figure, the location of the focal point for rays passing through the corneal periphery is a function of ‘how peripheral’ those rays are. Given this, how can one measure spherical aberration?
By convention, rays passing through the cornea 6 mm from the optical axis are used
?
?
?

## Slide 81
Aberrations: Spherical
(All these rays
are from the
same
point
on the object
at infinity.)
Optical
axis
Optical
axis
How much spherical aberration does the average human cornea possess?
About +0.27 mm
So this means the cornea possesses positive spherical aberration. But the cornea’s Q factor is negative. What gives?
The Q factor measures the relative asphericity of the cornea. A negative Q factor simply means the corneal periphery has less power than the central cornea; it does not mean the cornea as a whole doesn’t have spherical aberration!
Why is the unit of spherical aberration microns--a unit of distance? What distance is being referred to?
It refers to the distance between the location where central rays form a focal point and where the peripheral rays form a focal point
But as can be seen in the figure, the location of the focal point for rays passing through the corneal periphery is a function of ‘how peripheral’ those rays are. Given this, how can one measure spherical aberration?
By convention, rays passing through the cornea 6 mm from the optical axis are used
0.27 mm
3 mm
3 mm
(Drawing not to scale, obviously)

## Slide 82
(All these rays
are from the
same
point
on the object
at infinity.)
Optical
axis
Optical
axis
How much spherical aberration does the average human cornea possess?
About +0.27 mm
So this means the cornea possesses positive spherical aberration. But the cornea’s Q factor is negative. What gives?
The Q factor measures the relative asphericity of the cornea. A negative Q factor simply means the corneal periphery has less power than the central cornea; it does not mean the cornea as a whole doesn’t have spherical aberration!
Aberrations: Spherical

## Slide 83
(All these rays
are from the
same
point
on the object
at infinity.)
Optical
axis
Optical
axis
How much spherical aberration does the average human cornea possess?
About +0.27 mm
So this means the cornea possesses positive spherical aberration. But the cornea’s Q factor is negative. What gives?
The Q factor measures the relative asphericity of the cornea. A negative Q factor simply means the corneal periphery has less power than the central cornea; it does not mean the cornea as a whole doesn’t have spherical aberration!
Aberrations: Spherical

## Slide 84
(All these rays
are from the
same
point
on the object
at infinity.)
Spherical Aberration
Optical
axis
Optical
axis
How much spherical aberration does the average human cornea possess?
About +0.27 mm
So this means the cornea possesses positive spherical aberration. But the cornea’s Q factor is negative. What gives?
The Q factor measures the relative asphericity of the cornea. A negative Q factor simply means the corneal periphery has less power than the central cornea; it does not mean the cornea as a whole doesn’t have spherical aberration!
Recall that the cornea’s Q factor is -0.26. What would it be if the cornea had no spherical aberration?
About -0.52
Why didn’t we evolve corneas with a Q factor of -0.52?
Well, know one can say for sure of course. But what can be said with certainty is that a Q factor of -0.52 would require a radically different angle between the cornea and the sclera--an angle that could not be achieved given the biomechanics and size of the normal human globe. Thus, a Q factor of -0.52 would require a very radical ‘re-design’ of the globe--and thus of the orbits, and the cranium, and etc.

## Slide 85
(All these rays
are from the
same
point
on the object
at infinity.)
Spherical Aberration
Optical
axis
Optical
axis
How much spherical aberration does the average human cornea possess?
About +0.27 mm
So this means the cornea possesses positive spherical aberration. But the cornea’s Q factor is negative. What gives?
The Q factor measures the relative asphericity of the cornea. A negative Q factor simply means the corneal periphery has less power than the central cornea; it does not mean the cornea as a whole doesn’t have spherical aberration!
Recall that the cornea’s Q factor is -0.26. What would it be if the cornea had no spherical aberration?
About -0.52
Why didn’t we evolve corneas with a Q factor of -0.52?
Well, know one can say for sure of course. But what can be said with certainty is that a Q factor of -0.52 would require a radically different angle between the cornea and the sclera--an angle that could not be achieved given the biomechanics and size of the normal human globe. Thus, a Q factor of -0.52 would require a very radical ‘re-design’ of the globe--and thus of the orbits, and the cranium, and etc.

## Slide 86
(All these rays
are from the
same
point
on the object
at infinity.)
Spherical Aberration
Optical
axis
Optical
axis
How much spherical aberration does the average human cornea possess?
About +0.27 mm
So this means the cornea possesses positive spherical aberration. But the cornea’s Q factor is negative. What gives?
The Q factor measures the relative asphericity of the cornea. A negative Q factor simply means the corneal periphery has less power than the central cornea; it does not mean the cornea as a whole doesn’t have spherical aberration!
Recall that the cornea’s Q factor is -0.26. What would it be if the cornea had no spherical aberration?
About -0.52
Why didn’t we evolve corneas with a Q factor of -0.52?
Well, know one can say for sure of course. But what can be said with certainty is that a Q factor of -0.52 would require a radically different angle between the cornea and the sclera--an angle that could not be achieved given the biomechanics and size of the normal human globe. Thus, a Q factor of -0.52 would require a very radical ‘re-design’ of the globe--and thus of the orbits, and the cranium, and etc.

## Slide 87
(All these rays
are from the
same
point
on the object
at infinity.)
Spherical Aberration
Optical
axis
Optical
axis
How much spherical aberration does the average human cornea possess?
About +0.27 mm
So this means the cornea possesses positive spherical aberration. But the cornea’s Q factor is negative. What gives?
The Q factor measures the relative asphericity of the cornea. A negative Q factor simply means the corneal periphery has less power than the central cornea; it does not mean the cornea as a whole doesn’t have spherical aberration!
Recall that the cornea’s Q factor is -0.26. What would it be if the cornea had no spherical aberration?
About -0.52
Why didn’t we evolve corneas with a Q factor of -0.52?
Well, no one can say for sure of course. But what can be said with certainty is that a Q factor of -0.52 would require a radically different angle between the cornea and the sclera--an angle that could not be achieved given the biomechanics and size of the normal human globe. Thus, a Q factor of -0.52 would require a very radical ‘re-design’ of the globe--and thus of the orbits, and the cranium, and etc.

## Slide 88
(All these rays
are from the
same
point
on the object
at infinity.)
Spherical Aberration
Optical
axis
Optical
axis
How much spherical aberration does the average human cornea possess?
About +0.27 mm
So this means the cornea possesses positive spherical aberration. But the cornea’s Q factor is negative. What gives?
The Q factor measures the relative asphericity of the cornea. A negative Q factor simply means the corneal periphery has less power than the central cornea; it does not mean the cornea as a whole doesn’t have spherical aberration!
Recall that the cornea’s Q factor is -0.26. What would it be if the cornea had no spherical aberration?
About -0.52
Why didn’t we evolve corneas with a Q factor of -0.52?
Well, no one can say for sure of course. But what can be said with certainty is that a Q factor of -0.52 would require a radically different angle between the cornea and the sclera--an angle that could not be achieved given the biomechanics and size of the normal human globe. Thus, a Q factor of -0.52 would require a very radical ‘re-design’ of the globe--and thus of the orbits, and the cranium, and etc.

## Slide 89
(All these rays
are from the
same
point
on the object
at infinity.)
Spherical Aberration
Optical
axis
Optical
axis
How much spherical aberration does the average human cornea possess?
About +0.27 mm
So this means the cornea possesses positive spherical aberration. But the cornea’s Q factor is negative. What gives?
The Q factor measures the relative asphericity of the cornea. A negative Q factor simply means the corneal periphery has less power than the central cornea; it does not mean the cornea as a whole doesn’t have spherical aberration!
Recall that the cornea’s Q factor is -0.26. What would it be if the cornea had no spherical aberration?
About -0.52
Why didn’t we evolve corneas with a Q factor of -0.52?
Well, no one can say for sure of course. But what can be said with certainty is that a Q factor of -0.52 would require a radically different angle between the cornea and the sclera--an angle that could not be achieved given the biomechanics and size of the normal human globe. Thus, a Q factor of -0.52 would require a very radical ‘re-design’ of the globe--and thus of the orbits, and the cranium, and etc.
Interestingly, while we didn’t evolve corneas with a Q factor of -0.52, we did evolve eyes with it. The human lens of a young adult has an average Q value of about -0.25. Thus, the entire refracting system of the average young adult human eye has a total Q factor very close to -0.52, and thus has little to no spherical aberration!
eyes
We did!

## Slide 90
(All these rays
are from the
same
point
on the object
at infinity.)
Spherical Aberration
Optical
axis
Optical
axis
How much spherical aberration does the average human cornea possess?
About +0.27 mm
So this means the cornea possesses positive spherical aberration. But the cornea’s Q factor is negative. What gives?
The Q factor measures the relative asphericity of the cornea. A negative Q factor simply means the corneal periphery has less power than the central cornea; it does not mean the cornea as a whole doesn’t have spherical aberration!
Recall that the cornea’s Q factor is -0.26. What would it be if the cornea had no spherical aberration?
About -0.52
Why didn’t we evolve corneas with a Q factor of -0.52?
Well, no one can say for sure of course. But what can be said with certainty is that a Q factor of -0.52 would require a radically different angle between the cornea and the sclera--an angle that could not be achieved given the biomechanics and size of the normal human globe. Thus, a Q factor of -0.52 would require a very radical ‘re-design’ of the globe--and thus of the orbits, and the cranium, and etc.
Interestingly, while we didn’t evolve corneas with a Q factor of -0.52, we did evolve eyes with it. The human lens of a young adult has an average Q value of about -0.25. Thus, the entire refracting system of the average young adult human eye has a total Q factor very close to -0.52, and thus has little to no spherical aberration!
eyes
We did!
‘Young adult’ seems to be emphasized, implying that the Q factor is not -0.25 in older adults. What happens to the Q factor of the lens as we age?
It becomes progressively less negative, ultimately reaching a value of 0
at about age 40

## Slide 91
(All these rays
are from the
same
point
on the object
at infinity.)
Spherical Aberration
Optical
axis
Optical
axis
How much spherical aberration does the average human cornea possess?
About +0.27 mm
So this means the cornea possesses positive spherical aberration. But the cornea’s Q factor is negative. What gives?
The Q factor measures the relative asphericity of the cornea. A negative Q factor simply means the corneal periphery has less power than the central cornea; it does not mean the cornea as a whole doesn’t have spherical aberration!
Recall that the cornea’s Q factor is -0.26. What would it be if the cornea had no spherical aberration?
About -0.52
Why didn’t we evolve corneas with a Q factor of -0.52?
Well, no one can say for sure of course. But what can be said with certainty is that a Q factor of -0.52 would require a radically different angle between the cornea and the sclera--an angle that could not be achieved given the biomechanics and size of the normal human globe. Thus, a Q factor of -0.52 would require a very radical ‘re-design’ of the globe--and thus of the orbits, and the cranium, and etc.
Interestingly, while we didn’t evolve corneas with a Q factor of -0.52, we did evolve eyes with it. The human lens of a young adult has an average Q value of about -0.25. Thus, the entire refracting system of the average young adult human eye has a total Q factor very close to -0.52, and thus has little to no spherical aberration!
eyes
We did!
‘Young adult’ seems to be emphasized, implying that the Q factor is not -0.25 in older adults. What happens to the Q factor of the lens as we age?
It becomes progressively less negative, ultimately reaching a value of 0
at about age 40
more v less
#
#

## Slide 92
(All these rays
are from the
same
point
on the object
at infinity.)
Spherical Aberration
Optical
axis
Optical
axis
How much spherical aberration does the average human cornea possess?
About +0.27 mm
So this means the cornea possesses positive spherical aberration. But the cornea’s Q factor is negative. What gives?
The Q factor measures the relative asphericity of the cornea. A negative Q factor simply means the corneal periphery has less power than the central cornea; it does not mean the cornea as a whole doesn’t have spherical aberration!
Recall that the cornea’s Q factor is -0.26. What would it be if the cornea had no spherical aberration?
About -0.52
Why didn’t we evolve corneas with a Q factor of -0.52?
Well, no one can say for sure of course. But what can be said with certainty is that a Q factor of -0.52 would require a radically different angle between the cornea and the sclera--an angle that could not be achieved given the biomechanics and size of the normal human globe. Thus, a Q factor of -0.52 would require a very radical ‘re-design’ of the globe--and thus of the orbits, and the cranium, and etc.
Interestingly, while we didn’t evolve corneas with a Q factor of -0.52, we did evolve eyes with it. The human lens of a young adult has an average Q value of about -0.25. Thus, the entire refracting system of the average young adult human eye has a total Q factor very close to -0.52, and thus has little to no spherical aberration!
eyes
We did!
‘Young adult’ seems to be emphasized, implying that the Q factor is not -0.25 in older adults. What happens to the Q factor of the lens as we age?
It becomes progressively less negative, ultimately reaching a value of 0
at about age 40

## Slide 93
(All these rays
are from the
same
point
on the object
at infinity.)
Spherical Aberration
Optical
axis
Optical
axis
How much spherical aberration does the average human cornea possess?
About +0.27 mm
So this means the cornea possesses positive spherical aberration. But the cornea’s Q factor is negative. What gives?
The Q factor measures the relative asphericity of the cornea. A negative Q factor simply means the corneal periphery has less power than the central cornea; it does not mean the cornea as a whole doesn’t have spherical aberration!
Recall that the cornea’s Q factor is -0.26. What would it be if the cornea had no spherical aberration?
About -0.52
Why didn’t we evolve corneas with a Q factor of -0.52?
Well, no one can say for sure of course. But what can be said with certainty is that a Q factor of -0.52 would require a radically different angle between the cornea and the sclera--an angle that could not be achieved given the biomechanics and size of the normal human globe. Thus, a Q factor of -0.52 would require a very radical ‘re-design’ of the globe--and thus of the orbits, and the cranium, and etc.
Interestingly, while we didn’t evolve corneas with a Q factor of -0.52, we did evolve eyes with it. The human lens of a young adult has an average Q value of about -0.25. Thus, the entire refracting system of the average young adult human eye has a total Q factor very close to -0.52, and thus has little to no spherical aberration!
eyes
We did!
What characteristic of older eyes—quite frustrating for anyone attempting to retinoscope them—serves to offset the spherical-aberration-inducing loss of negative Q factor in the lens?
The pupil tends to be miotic, which blocks the more peripheral rays
‘Young adult’ seems to be emphasized, implying that the Q factor is not -0.25 in older adults. What happens to the Q factor of the lens as we age?
It becomes progressively less negative, ultimately reaching a value of 0
at about age 40

## Slide 94
(All these rays
are from the
same
point
on the object
at infinity.)
Spherical Aberration
Optical
axis
Optical
axis
How much spherical aberration does the average human cornea possess?
About +0.27 mm
So this means the cornea possesses positive spherical aberration. But the cornea’s Q factor is negative. What gives?
The Q factor measures the relative asphericity of the cornea. A negative Q factor simply means the corneal periphery has less power than the central cornea; it does not mean the cornea as a whole doesn’t have spherical aberration!
Recall that the cornea’s Q factor is -0.26. What would it be if the cornea had no spherical aberration?
About -0.52
Why didn’t we evolve corneas with a Q factor of -0.52?
Well, no one can say for sure of course. But what can be said with certainty is that a Q factor of -0.52 would require a radically different angle between the cornea and the sclera--an angle that could not be achieved given the biomechanics and size of the normal human globe. Thus, a Q factor of -0.52 would require a very radical ‘re-design’ of the globe--and thus of the orbits, and the cranium, and etc.
Interestingly, while we didn’t evolve corneas with a Q factor of -0.52, we did evolve eyes with it. The human lens of a young adult has an average Q value of about -0.25. Thus, the entire refracting system of the average young adult human eye has a total Q factor very close to -0.52, and thus has little to no spherical aberration!
eyes
We did!
What characteristic of older eyes—quite frustrating for anyone attempting to retinoscope them—serves to offset the spherical-aberration-inducing loss of negative Q factor in the lens?
The pupil tends to be miotic, which blocks the more peripheral rays
‘Young adult’ seems to be emphasized, implying that the Q factor is not -0.25 in older adults. What happens to the Q factor of the lens as we age?
It becomes progressively less negative, ultimately reaching a value of 0
at about age 40

## Slide 95
(All these rays
are from the
same
point
on the object
at infinity.)
Spherical Aberration
Optical
axis
Optical
axis
How much spherical aberration does the average human cornea possess?
About +0.27 mm
So this means the cornea possesses positive spherical aberration. But the cornea’s Q factor is negative. What gives?
The Q factor measures the relative asphericity of the cornea. A negative Q factor simply means the corneal periphery has less power than the central cornea; it does not mean the cornea as a whole doesn’t have spherical aberration!
Recall that the cornea’s Q factor is -0.26. What would it be if the cornea had no spherical aberration?
About -0.52
Why didn’t we evolve corneas with a Q factor of -0.52?
Well, no one can say for sure of course. But what can be said with certainty is that a Q factor of -0.52 would require a radically different angle between the cornea and the sclera--an angle that could not be achieved given the biomechanics and size of the normal human globe. Thus, a Q factor of -0.52 would require a very radical ‘re-design’ of the globe--and thus of the orbits, and the cranium, and etc.
So, the average cornea has a spherical aberration of +0.27 mm and a Q factor of -0.26. Surely it’s not a coincidence that these numbers almost perfectly cancel one another out?
I’m afraid that’s exactly what it is--a coincidence

## Slide 96
(All these rays
are from the
same
point
on the object
at infinity.)
Spherical Aberration
Optical
axis
Optical
axis
How much spherical aberration does the average human cornea possess?
About +0.27 mm
So this means the cornea possesses positive spherical aberration. But the cornea’s Q factor is negative. What gives?
The Q factor measures the relative asphericity of the cornea. A negative Q factor simply means the corneal periphery has less power than the central cornea; it does not mean the cornea as a whole doesn’t have spherical aberration!
Recall that the cornea’s Q factor is -0.26. What would it be if the cornea had no spherical aberration?
About -0.52
Why didn’t we evolve corneas with a Q factor of -0.52?
Well, no one can say for sure of course. But what can be said with certainty is that a Q factor of -0.52 would require a radically different angle between the cornea and the sclera--an angle that could not be achieved given the biomechanics and size of the normal human globe. Thus, a Q factor of -0.52 would require a very radical ‘re-design’ of the globe--and thus of the orbits, and the cranium, and etc.
So, the average cornea has a spherical aberration of +0.27 mm and a Q factor of -0.26. Surely it’s not a coincidence that these numbers almost perfectly cancel one another out?
I’m afraid that’s exactly what it is--a coincidence

## Slide 97
Aberrations: Zernike Polynomials
A mathematical system for describing and systematizing optical aberrations

## Slide 98
Aberrations: Zernike Polynomials
A mathematical system for describing and systematizing optical aberrations
  A series of shapes; when combined, they can account for the overall contour of a wavefront

## Slide 99
Aberrations: Zernike Polynomials
A mathematical system for describing and systematizing optical aberrations
  A series of shapes; when combined, they can account for the overall contour of a wavefront

## Slide 100
Aberrations: Zernike Polynomials
A mathematical system for describing and systematizing optical aberrations
  A series of shapes; when combined, they can account for the overall contour of a wavefront
In other words: Any wavefront, no matter how complex its shape, can be ‘broken down’ into a set of Zernike shapes.

## Slide 101
Aberrations: Zernike Polynomials
A mathematical system for describing and systematizing optical aberrations
  A series of shapes; when combined, they can account for the overall contour of a wavefront
  The set of shapes starts off very simple/basic, becoming progressively more complex as the series proceeds

## Slide 102
Aberrations: Zernike Polynomials
A mathematical system for describing and systematizing optical aberrations
  A series of shapes; when combined, they can account for the overall contour of a wavefront
  The set of shapes starts off very simple/basic, becoming progressively more complex as the series proceeds
    The progression is described by the order of a given shape

## Slide 103
Aberrations: Zernike Polynomials
A mathematical system for describing and systematizing optical aberrations
  A series of shapes; when combined, they can account for the overall contour of a wavefront
  The set of shapes starts off very simple/basic, becoming progressively more complex as the series proceeds
    The progression is described by the order of a given shape

## Slide 104
Aberrations: Zernike Polynomials
A mathematical system for describing and systematizing optical aberrations
  A series of shapes; when combined, they can account for the overall contour of a wavefront
  The set of shapes starts off very simple/basic, becoming progressively more complex as the series proceeds
    The progression is described by the order of a given shape
      Order start at zero, and goes up from there
#

## Slide 105
Aberrations: Zernike Polynomials
A mathematical system for describing and systematizing optical aberrations
  A series of shapes; when combined, they can account for the overall contour of a wavefront
  The set of shapes starts off very simple/basic, becoming progressively more complex as the series proceeds
    The progression is described by the order of a given shape
      Order start at zero, and goes up from there

## Slide 106
Defocus
Cylinder
Zernike Polynomial Order
Positive defocus
Negative defocus
Spherical
aberration
Coma
Trefoil
(Others, less
clinically relevant)
Aberrations: Zernike Polynomials
New Lingo
2nd
2nd
4th
3rd
3rd
Intentionally out of order! While coma and trefoil are of lower-order than spherical aberration, SA is clinically more significant.
Shape

## Slide 107
Defocus
Cylinder
Zernike Polynomial Order
Positive defocus
Negative defocus
Spherical
aberration
Coma
Trefoil
(Others, less
clinically relevant)
Aberrations: Zernike Polynomials
New Lingo
2nd
2nd
4th
3rd
3rd
Wait--you said ZPs start at zero and go up from there. What are the 0th and 1st-order aberrations?
?
0th
?
1st
Shape

## Slide 108
Defocus
Cylinder
Zernike Polynomial Order
Positive defocus
Negative defocus
Spherical
aberration
Coma
Trefoil
(Others, less
clinically relevant)
Aberrations: Zernike Polynomials
New Lingo
2nd
2nd
4th
3rd
3rd
0th
1st
‘Piston’
‘Prism’
Wait--you said ZPs start at zero and go up from there. What are the 0th and 1st-order aberrations?
‘Piston’ and ‘prism’
Shape
(aka tip and tilt)

## Slide 109
Defocus
Cylinder
Zernike Polynomial Order
Positive defocus
Negative defocus
Spherical
aberration
Coma
Trefoil
(Others, less
clinically relevant)
Aberrations: Zernike Polynomials
New Lingo
2nd
2nd
4th
3rd
3rd
0th
1st
‘Piston’
‘Prism’
Shape
(aka tip and tilt)
Wait--you said ZPs start at zero and go up from there. What are the 0th and 1st-order aberrations?
‘Piston’ and ‘prism’
Why haven’t we talked about piston and prism?
Because while they are technically aberrations in the ZP system, they do not degrade the quality of the visual image, and are thus clinically irrelevant

## Slide 110
Defocus
Cylinder
Zernike Polynomial Order
Positive defocus
Negative defocus
Spherical
aberration
Coma
Trefoil
(Others, less
clinically relevant)
Aberrations: Zernike Polynomials
New Lingo
2nd
2nd
4th
3rd
3rd
0th
1st
‘Piston’
‘Prism’
Shape
Why haven’t we talked about piston and prism?
Because while they are technically aberrations in the ZP system, they do not degrade the quality of the visual image and are thus clinically irrelevant
(aka tip and tilt)
Wait--you said ZPs start at zero and go up from there. What are the 0th and 1st-order aberrations?
‘Piston’ and ‘prism’

## Slide 111
Defocus
Cylinder
Zernike Polynomial Order
Positive defocus
Negative defocus
Spherical
aberration
Coma
Trefoil
(Others, less
clinically relevant)
Aberrations: Zernike Polynomials
New Lingo
2nd
2nd
4th
3rd
3rd
0th
1st
‘Piston’
‘Prism’
Shape
Myopia
Hyperopia
=
=
(positive)
‘Bowl’

## Slide 112
Defocus
Cylinder
Zernike Polynomial Order
Positive defocus
Negative defocus
Spherical
aberration
Coma
Trefoil
(Others, less
clinically relevant)
Aberrations: Zernike Polynomials
New Lingo
2nd
2nd
4th
3rd
3rd
0th
1st
‘Piston’
‘Prism’
Shape
Myopia
Hyperopia
=
=
‘Saddle’

## Slide 113
Defocus
Cylinder
Zernike Polynomial Order
Positive defocus
Negative defocus
Spherical
aberration
Coma
Trefoil
(Others, less
clinically relevant)
Aberrations: Zernike Polynomials
New Lingo
2nd
2nd
4th
3rd
3rd
0th
1st
‘Piston’
‘Prism’
Shape
Myopia
Hyperopia
=
=
‘Bundt cake pan’

## Slide 114
Defocus
Cylinder
Zernike Polynomial Order
Positive defocus
Negative defocus
Spherical
aberration
Coma
Trefoil
(Others, less
clinically relevant)
Aberrations: Zernike Polynomials
New Lingo
2nd
2nd
4th
3rd
3rd
0th
1st
‘Piston’
‘Prism’
Shape
Myopia
Hyperopia
=
=
‘Recliner’

## Slide 115
Defocus
Cylinder
Zernike Polynomial Order
Positive defocus
Negative defocus
Spherical
aberration
Coma
Trefoil
(Others, less
clinically relevant)
Aberrations: Zernike Polynomials
New Lingo
2nd
2nd
4th
3rd
3rd
0th
1st
‘Piston’
‘Prism’
Shape
Myopia
Hyperopia
=
=
‘Recliner’
In layman’s terms, what is the problem with the incoming light that leads to the higher-order aberration of coma?
Coma occurs when the source of the rays is located off the optical axis. Because of its location, light from this source reaches one side of the pupil before the other. The result is that rays entering the ‘near’ side and the ‘far’ side of the pupil are focused not at as a single point, but rather as a point with a ‘smear’ attached (not unlike a comet’s tail, which is why the words share a root).

## Slide 116
Defocus
Cylinder
Zernike Polynomial Order
Positive defocus
Negative defocus
Spherical
aberration
Coma
Trefoil
(Others, less
clinically relevant)
Aberrations: Zernike Polynomials
New Lingo
2nd
2nd
4th
3rd
3rd
0th
1st
‘Piston’
‘Prism’
Shape
Myopia
Hyperopia
=
=
‘Recliner’
In layman’s terms, what is the problem with the incoming light that leads to the higher-order aberration of coma?
Coma occurs when the source of the rays is located off the optical axis. Because of its location, light from this source reaches one side of the pupil before the other. The result is that rays entering the ‘near’ side and the ‘far’ side of the pupil are focused not at as a single point, but rather as a point with a ‘smear’ attached (not unlike a comet’s tail, which is why the words share a root).

## Slide 117
Defocus
Cylinder
Zernike Polynomial Order
Positive defocus
Negative defocus
Spherical
aberration
Coma
Trefoil
(Others, less
clinically relevant)
Aberrations: Zernike Polynomials
New Lingo
2nd
2nd
4th
3rd
3rd
0th
1st
‘Piston’
‘Prism’
Shape
Myopia
Hyperopia
=
=
‘Recliner’
In layman’s terms, what is the problem with the incoming light that leads to the higher-order aberration of coma?
Coma occurs when the source of the rays is located off the optical axis. Because of its location, light from this source reaches one side of the pupil before the other. The result is that rays entering the ‘near’ side and the ‘far’ side of the pupil are focused not at as a single point, but rather as a point with a ‘smear’ attached (not unlike a comet’s tail, which is why the words share a root).

## Slide 118
Defocus
Cylinder
Zernike Polynomial Order
Positive defocus
Negative defocus
Spherical
aberration
Coma
Trefoil
(Others, less
clinically relevant)
Aberrations: Zernike Polynomials
New Lingo
2nd
2nd
4th
3rd
3rd
0th
1st
‘Piston’
‘Prism’
Shape
Myopia
Hyperopia
=
=
‘Three peaks’

## Slide 119
Defocus
Cylinder
Zernike Polynomial Order
Positive defocus
Negative defocus
Spherical
aberration
Coma
Trefoil
(Others, less
clinically relevant)
Aberrations: Zernike Polynomials
New Lingo
2nd
2nd
4th
3rd
3rd
0th
1st
‘Piston’
‘Prism’
Shape
Myopia
Hyperopia
=
=
‘Three peaks’
In layman’s terms, what is the problem with the incoming light that leads to trefoil?
Happily, the BCSC books do not spend much time on trefoil, so you don’t need to know much more about it than:
1) it is a clinically significant (albeit modestly so) higher-order aberration; and
2) its shape, ie, be able to recognize its wavefront analysis profile (more on this later).

## Slide 120
Defocus
Cylinder
Zernike Polynomial Order
Positive defocus
Negative defocus
Spherical
aberration
Coma
Trefoil
(Others, less
clinically relevant)
Aberrations: Zernike Polynomials
New Lingo
2nd
2nd
4th
3rd
3rd
0th
1st
‘Piston’
‘Prism’
Shape
Myopia
Hyperopia
=
=
‘Three peaks’
In layman’s terms, what is the problem with the incoming light that leads to trefoil?
Happily, the BCSC books do not spend much time on trefoil, so you don’t need to know much more about it than:
1) it is a clinically significant (albeit modestly so) higher-order aberration; and
2) its shape, ie, be able to recognize its wavefront analysis profile (more on this later).

## Slide 121
3-D representation
3-D representation
0th
1st
2nd
3rd
4th
Spherical
aberration
Aberrations: Zernike Polynomials
In addition to the 3-D representation of each shape…
You need to be able to recognize its 2-D image as well!

## Slide 122
3-D representation
0th
1st
2nd
3rd
4th
Spherical
aberration
2-D representation
In addition to the 3-D representation of each shape…
You need to be able to recognize its 2-D image as well!
Aberrations: Zernike Polynomials

## Slide 123
3-D representation
0th
1st
2nd
3rd
4th
Spherical
aberration
2-D representation
Aberrations: Zernike Polynomials
And in addition to the 2- and 3-D representation of each shape…

## Slide 124
Spherical
aberration
2-D representation
Optical effect of each
0th
1st
2nd
3rd
4th
(Note that coma looks like a comet)
(As mentioned previously, note that piston, tip and tilt do not degrade the quality of the image)
Aberrations: Zernike Polynomials
And in addition to the 2- and 3-D representation of each shape…
You need to be able to recognize its optical impact on an image-point

## Slide 125
Aberrations
Wavefront-guided keratorefractive surgery did away with the second problem
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected even if they had been measureable
two-words

## Slide 126
Aberrations
Wavefront-guided keratorefractive surgery did away with the second problem
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected even if they had been measureable

## Slide 127
Aberrations
Wavefront-guided keratorefractive surgery did away with the second problem
  Allows surgeons to correct/minimize the higher-order aberrations identified via wavefront analysis
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected even if they had been measureable

## Slide 128
Aberrations
Wavefront-guided keratorefractive surgery did away with the second problem
  Allows surgeons to correct/minimize the higher-order aberrations identified via wavefront analysis
  That said, precisely which higher-order aberrations should be corrected (and to what degree) is an unsettled issue at this time
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected even if they had been measureable

## Slide 129
Aberrations
Wavefront-guided keratorefractive surgery did away with the second problem
  Allows surgeons to correct/minimize the higher-order aberrations identified via wavefront analysis
  That said, precisely which higher-order aberrations should be corrected (and to what degree) is an unsettled issue at this time
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected even if they had been measureable
How does a wavefront-guided ablative procedure differ from a wavefront-optimized ablative procedure?
In a wavefront-guided procedure, the information obtained from wavefront analysis is used to correct certain higher-order aberrations along with the more-important lower-order (ie, sphere and cyl) aberrations.
In contrast, a wavefront-optimized procedure corrects only sphere and cylinder; no attempt is made to address higher-order aberrations. Instead, the wavefront information is used to ‘fine tune’ the ablation in such a way as to minimize the creation or exacerbation of higher-order aberrations.

## Slide 130
Aberrations
Wavefront-guided keratorefractive surgery did away with the second problem
  Allows surgeons to correct/minimize the higher-order aberrations identified via wavefront analysis
  That said, precisely which higher-order aberrations should be corrected (and to what degree) is an unsettled issue at this time
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected even if they had been measureable
How does a wavefront-guided ablative procedure differ from a wavefront-optimized ablative procedure?
In a wavefront-guided procedure, the information obtained from wavefront analysis is used to correct certain higher-order aberrations along with the more-important lower-order (ie, sphere and cyl) aberrations.
In contrast, a wavefront-optimized procedure corrects only sphere and cylinder; no attempt is made to address higher-order aberrations. Instead, the wavefront information is used to ‘fine tune’ the ablation in such a way as to minimize the creation or exacerbation of higher-order aberrations.

## Slide 131
Aberrations
Wavefront-guided keratorefractive surgery did away with the second problem
  Allows surgeons to correct/minimize the higher-order aberrations identified via wavefront analysis
  That said, precisely which higher-order aberrations should be corrected (and to what degree) is an unsettled issue at this time
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected even if they had been measureable
How does a wavefront-guided ablative procedure differ from a wavefront-optimized ablative procedure?
In a wavefront-guided procedure, the information obtained from wavefront analysis is used to correct certain higher-order aberrations along with the more-important lower-order (ie, sphere and cyl) aberrations.
In contrast, a wavefront-optimized procedure corrects only sphere and cylinder; no attempt is made to address higher-order aberrations. Instead, the wavefront information is used to ‘fine tune’ the ablation in such a way as to minimize the creation or exacerbation of higher-order aberrations.

## Slide 132
Aberrations
Wavefront-guided keratorefractive surgery did away with the second problem
  Allows surgeons to correct/minimize the higher-order aberrations identified via wavefront analysis
  That said, precisely which higher-order aberrations should be corrected (and to what degree) is an unsettled issue at this time
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected even if they had been measureable
How does a wavefront-guided ablative procedure differ from a wavefront-optimized ablative procedure?
In a wavefront-guided procedure, the information obtained from wavefront analysis is used to correct certain higher-order aberrations along with the more-important lower-order (ie, sphere and cyl) aberrations.
In contrast, a wavefront-optimized procedure corrects only sphere and cylinder; no attempt is made to address higher-order aberrations. Instead, the wavefront information is used to ‘fine tune’ the ablation in such a way as to minimize the creation or exacerbation of higher-order aberrations.
How does a wavefront-optimized ablative procedure differ from a so-called conventional ablative procedure?
In a conventional procedure, the ablation is determined solely by a standard phoropter-based refraction obtained by the surgeon during pre-op. That is, the phoropter-based refraction is used to program the correction of sphere and cyl. In a wavefront-optimized ablation, the wavefront analysis is used to program the correxction of sphere and cyl.

## Slide 133
Aberrations
Wavefront-guided keratorefractive surgery did away with the second problem
  Allows surgeons to correct/minimize the higher-order aberrations identified via wavefront analysis
  That said, precisely which higher-order aberrations should be corrected (and to what degree) is an unsettled issue at this time
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected even if they had been measureable
How does a wavefront-guided ablative procedure differ from a wavefront-optimized ablative procedure?
In a wavefront-guided procedure, the information obtained from wavefront analysis is used to correct certain higher-order aberrations along with the more-important lower-order (ie, sphere and cyl) aberrations.
In contrast, a wavefront-optimized procedure corrects only sphere and cylinder; no attempt is made to address higher-order aberrations. Instead, the wavefront information is used to ‘fine tune’ the ablation in such a way as to minimize the creation or exacerbation of higher-order aberrations.
How does a wavefront-optimized ablative procedure differ from a so-called conventional ablative procedure?
In a conventional procedure, the ablation is determined solely by a standard phoropter-based refraction obtained by the surgeon during pre-op. That is, the phoropter-based refraction is used to program the correction of sphere and cyl. In a wavefront-optimized ablation, the wavefront analysis is used to program the correction of sphere and cyl.

## Slide 134
Aberrations
Wavefront-guided keratorefractive surgery did away with the second problem
  Allows surgeons to correct/minimize the higher-order aberrations identified via wavefront analysis
  That said, precisely which higher-order aberrations should be corrected (and to what degree) is an unsettled issue at this time
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected even if they had been measureable
How does a wavefront-guided ablative procedure differ from a wavefront-optimized ablative procedure?
In a wavefront-guided procedure, the information obtained from wavefront analysis is used to correct certain higher-order aberrations along with the more-important lower-order (ie, sphere and cyl) aberrations.
In contrast, a wavefront-optimized procedure corrects only sphere and cylinder; no attempt is made to address higher-order aberrations. Instead, the wavefront information is used to ‘fine tune’ the ablation in such a way as to minimize the creation or exacerbation of higher-order aberrations.
How does a wavefront-optimized ablative procedure differ from a so-called conventional ablative procedure?
In a conventional procedure, the ablation is determined solely by a standard phoropter-based refraction obtained by the surgeon during pre-op. That is, the phoropter-based refraction is used to program the correction of sphere and cyl. In a wavefront-optimized ablation, the wavefront analysis is used to program the correction of sphere and cyl.
In addition to wavefront-guided, wavefront-optimized and conventional approaches to ablation, there is one more. What is it?
Topography-guided. For details on this and the other three approaches, see the slide set on Photoablative Refractive Surgery.

## Slide 135
Aberrations
Wavefront-guided keratorefractive surgery did away with the second problem
  Allows surgeons to correct/minimize the higher-order aberrations identified via wavefront analysis
  That said, precisely which higher-order aberrations should be corrected (and to what degree) is an unsettled issue at this time
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected even if they had been measureable
How does a wavefront-guided ablative procedure differ from a wavefront-optimized ablative procedure?
In a wavefront-guided procedure, the information obtained from wavefront analysis is used to correct certain higher-order aberrations along with the more-important lower-order (ie, sphere and cyl) aberrations.
In contrast, a wavefront-optimized procedure corrects only sphere and cylinder; no attempt is made to address higher-order aberrations. Instead, the wavefront information is used to ‘fine tune’ the ablation in such a way as to minimize the creation or exacerbation of higher-order aberrations.
How does a wavefront-optimized ablative procedure differ from a so-called conventional ablative procedure?
In a conventional procedure, the ablation is determined solely by a standard phoropter-based refraction obtained by the surgeon during pre-op. That is, the phoropter-based refraction is used to program the correction of sphere and cyl. In a wavefront-optimized ablation, the wavefront analysis is used to program the correction of sphere and cyl.
In addition to wavefront-guided, wavefront-optimized and conventional approaches to ablation, there is one more. What is it?
Topography-guided. For details on this and the other three approaches, see the slide set on Photoablative Refractive Surgery.

## Slide 136
Aberrations
Wavefront-guided keratorefractive surgery did away with the second problem
  Allows surgeons to correct/minimize the higher-order aberrations identified via wavefront analysis
  That said, precisely which higher-order aberrations should be corrected (and to what degree) is an unsettled issue at this time
Essentially, irregular astigmatism was a wastebasket term for aberrations that:
could not be measured in the clinic; and
could not be corrected even if they had been measureable
How does a wavefront-guided ablative procedure differ from a wavefront-optimized ablative procedure?
In a wavefront-guided procedure, the information obtained from wavefront analysis is used to correct certain higher-order aberrations along with the more-important lower-order (ie, sphere and cyl) aberrations.
In contrast, a wavefront-optimized procedure corrects only sphere and cylinder; no attempt is made to address higher-order aberrations. Instead, the wavefront information is used to ‘fine tune’ the ablation in such a way as to minimize the creation or exacerbation of higher-order aberrations.
How does a wavefront-optimized ablative procedure differ from a so-called conventional ablative procedure?
In a conventional procedure, the ablation is determined solely by a standard phoropter-based refraction obtained by the surgeon during pre-op. That is, the phoropter-based refraction is used to program the correction of sphere and cyl. In a wavefront-optimized ablation, the wavefront analysis is used to program the correction of sphere and cyl.
In addition to wavefront-guided, wavefront-optimized and conventional approaches to ablation, there is one more. What is it?
Topography-guided. For details on this and the other three approaches, see the slide set on Photoablative Refractive Surgery.
So, there are four basic techniques for performing keratoablative refractive surgery